## Slide 1: Connections

## Slide 2: Serial data

## Slide 3: Serial Terminals

## Slide 4: Serial connections
Telecommunication History 101
  RS-232
    DTE – Data Terminal Equipment
      Teletype
      Computer
    DCE – Data Communications Equipment
      Modems
    Send
    Receive

## Slide 6: Computer to Computer?
What if equipment close by?
  Direct DTE-DTE
Conflict of signals!
  Receive to receive
  Send to send - !!!!
Solution:
  Use a “null” modem

## Slide 7: Configuration
Must configure to connect:
  Correct Speed
    110, 300, 1200, 2400, 4800, 9600, etc.
  Number of bits
    7 or 8
  Parity
    None, even, odd, mark, space
  Stop bits
    1 or 2
Most modern devices default:
  9600-8-n-1

## Slide 8: Ethernet

## Slide 9: Ethernet

## Slide 10: Ethernet
Standard cable and jack
RJ-45 (8 pins)
  Send on 1-2
    + P1
    - P2
  Receive on 3-6
    + P3
    - P6

## Slide 11: Ethernet + Power
Power over Ethernet
  Add power to the spare wires

## Slide 12: EIA/TIA 568A and B
568A WIRING STANDARD
568B WIRING STANDARD
Note: Only pairs 2 and 3 are used for Standard Ethernet wiring. Pairs 1 and 4 can be used for other purposes such as telephones or even a second separate, complete Ethernet connection.
PIN | WIRE COLOR
1 | White w/Green Stripe
2 | Green w/White Stripe
3 | White w/Orange Stripe
4 | Blue w/White Stripe
5 | White w/Blue Stripe
6 | Orange w/White Stripe
7 | White w/Brown Stripe
8 | Brown w/White Stripe
PIN | WIRE COLOR
1 | White w/Orange Stripe
2 | Orange w/White Stripe
3 | White w/Green Stripe
4 | Blue w/White Stripe
5 | White w/Blue Stripe
6 | Green w/White Stripe
7 | White w/Brown Stripe
8 | Brown w/White Stripe

## Slide 13: EIA/TIA Cable pairings

## Slide 14: Two Ethernets over one cable
Pin No. | conductor color | Name
1 | white and orange | TX_D1+
2 | orange | TX_D1-
3 | white and green | RX_D2+
4 | blue | BI_D3+ **
5 | white and blue | BI_D3- **
6 | green | RX_D2-
7 | white and brown | BI_D4+ **
8 | brown | BI_D4- **
Use pairs 1 and 4 for the second Ethernet connection

## Slide 15: Ethernet Wiring Conventions
Note:
  PC (NIC) side “opposite” definitions than the switch or router side
  Colors may change

## Slide 16: “typical” connection
PC
PC
Networking Device
No problem!

## Slide 17: PC to PC?
Big problem!
  PC 1 Receive connected to PC2 Receive
Bigger problem!
  PC1 Transmit connected to PC2 Transmit!
PC1
PC2

## Slide 18: PC to PC Solution
Crossover cable

## Slide 19: Auto Sense
Some devices “auto sense” and set up the proper connections