## Slide 1: DNS
Domain Name Systems
Introduction

## Slide 2: DNS
DNS is not needed for the Internet to work
  IP addresses are all that is needed
  Computers have no problems remembering numbers
The internet would be extremely difficult for humans to use without DNS
  Who can remember
    74.125.138.105 is Google
    54.239.25.200 is Amazon
    173.252.120.68 is Facebook
    etc…

## Slide 3: History

## Slide 4: History
Human-legible abstraction of numerical addresses predates TCP/IP
  Even before the ARPAnet era
DNS invented in 1983, shortly after TCP/IP was deployed
  Original system: Hosts file
    Each computer on the network retrieved a file called HOSTS.TXT
    From a computer at SRI (now SRI International).
    The HOSTS.TXT file mapped numerical addresses to names.
  Hosts files still exists on most modern operating systems
    By default or through configuration
    Users can specify an IP address to use for a hostname without checking DNS
    Today Hosts file serves primarily for
      Troubleshooting DNS errors
      Mapping local addresses to more organic names
  Systems based on a hosts file have inherent limitations
    Every time a given computer's address changed
    Every computer accessing it would need an update to its hosts file
On Windows: C:\WINDOWS\system32\drivers\etc>

## Slide 5: History
Growth of networking called for a more scalable system
  Record changes of a host's address in one place only
  Other hosts would learn about the change dynamically through a notification system
  Completes a globally accessible network of:
    all hosts' names
      associated IP Addresses

## Slide 6: History
At the request of Jon Postel:
  Paul Mockapetris invented the Domain Name System in 1983
  Wrote the first implementation
Original specifications appear in RFC 882 and 883
  In 1987 RFC 1034 and RFC 1035 updated the DNS specification
    Made RFC 882 and RFC 883 obsolete
  Several more-recent RFCs have proposed various extensions to the core DNS protocols

## Slide 7: History
Four Berkeley students1 wrote the first UNIX implementation
  1984
  1985
    Kevin Dunlap (DEC) significantly re-wrote the DNS implementation
    Renamed it BIND (Berkeley Internet Name Domain)
  BIND ported to Windows NT platform early 1990s
BIND has a history of security issues and exploits
  Several alternative nameserver/resolver programs have been written and distributed in recent years
1Douglas Terry, Mark Painter, David Riggle and Songnian Zhou

## Slide 8: DNS Overview

## Slide 9: Domain name Servers (DNS)
Important but invisible part of the internet
  Might even say it is critical
Forms one of the largest databases

## Slide 10: Domain name Servers (DNS)
Every machine on a network is assigned a unique address
   every machine on the Internet has a unique address
IP addresses
  IPv4
    32 bit number and is expressed as 4 octets
  IPv4 addresses a.k.a. “Dotted Decimal Notation“
    AKA “dotted quad”
    Typical address format: 199.249.150.4
      Note: may also be written in hex: c7.f9.96.04

## Slide 11: Domain name Servers (DNS)
Human Oriented
  Difficult to remember IP addresses of websites
    Who is 66.135.221.10?
      Not easy to remember strings of numbers
    www.ebay.com
      Humans more easily remember words or names
  Domain names help
    To connect to a particular site:
      Enter its URL
        (Universal Resource Locator)
      DNS gets the mappings of the IP addresses and the corresponding names

## Slide 12: Names and Numbers

## Slide 13: Getting IP addresses
Basically, DNS converts machine names to IP addresses
  E.g. www.xyz.com  199.249.150.9
    Host and domain name to an IP address
Overall translates:
  Given a name it returns an IP address
    Main task
  Given an IP address it returns a name
    Mapping from an IP address to a machine name is called reverse mapping

## Slide 14: Example
Browser needs to access the web server at http://www.xyz.com
  Need the IP address of www.xyz.com
    Uses a directory service to look up the IP addresses
    DNS performs that service

## Slide 15: Example
To find www.xyz.com
  First: contact a DNS server
  Asks it to find the IP address for www.xyz.com
    DNS server has the address
    - or -
    DNS server might need to contact other DNS servers on the internet
      Etc., etc., etc….
  DNS is considered as a global network of servers

## Slide 16: Side note
One great advantage of DNS is that no single organization is responsible for updating/maintaining it
  Owners of the domain are responsible for maintaining proper IP addresses for their machines
It is truly a distributed database

## Slide 17: Resume 2/13

## Slide 18: 2 and 3 letter TLD names?
TLD – Top Level Domain

## Slide 19: Domains
DNS server
  Computer that's running the DNS software
    Dozens of DNS programs
      https://en.wikipedia.org/wiki/Comparison_of_DNS_server_software
    Most popular DNS software is BIND (Berkeley Internet Name Domain)
      BIND9 “latest”
      BIND 10 currently an unsupported open source project

## Slide 20: Domains
DNS is hierarchical, tree-structured system
  Top domain is denoted by '.'
    That is: a single period or dot
    Known as the root of the system
  Major “sub” domain types
    Top Level Domains (TLD)
    Original Top Level Domains
      Seven generic domains:
        ‘.com', ‘.org', ‘.gov', ‘.mil', ‘.net', ‘.edu', ‘.int‘
    140+ country domains:
      ‘.us’, ‘.ca’, ‘.uk’, ‘.tv’, etc…
    Others (ICANN era)
      ‘.biz’, ‘.bio’, ‘.cash’, ‘.pizza’, …
    List_of_Internet_top-level_domains

## Slide 21: Components

## Slide 22: Components
Two basic components
  Name server
  Resolver

## Slide 23: Name server
Looks up the names
  Usually one name server for a cluster of machines
    If the name server does not contain the requested information
      it will contact another name server

## Slide 24: Nameserver
It is not required for every server to know how to contact every other server
  Every name server will know how to contact the root name server ( . )
  In turn will know the location of every authoritative name server for all the top level domains

## Slide 25: Resolver:
Runs on a client machine
  Initiates DNS lookups
  Contains a list of name servers to use
Function of each of these name servers is to resolve name queries

## Slide 26: Resolver:
Three types of name servers
  Primary name server
  Secondary name server
  Caching name server

## Slide 27: Resolver:
Primary name servers own the database records
  Changes are propagated via a 'zone transfer‘
Secondary name servers are configured for backup purposes
  Any changes to primary name servers needs to be propagated to secondary name servers

## Slide 28: Resolver:
Caching name servers
  Only resolve name queries
    Remember the results of previous queries
  Do not maintain any DNS database files

## Slide 29: Caching

## Slide 30: Caching
DNS uses principle of 'caching' for its operation
  When a name server receives information about a mapping
    It caches this information
  Further queries for the same mapping will use this cached result
    For a set time
    Reducing the search cost

## Slide 31: Caching
Name servers don't cache forever
  Caching has a time to live (TTL)
    TTL determines how long a server will cache a piece of information
  When a name servers cache receive an IP address
    It receives the TTL with it
  Name server caches the IP address for the period of time then discards it
Note: this TTL is different than the routing TTL you see in a ping

## Slide 32: Caching
When a process needs to determine an IP address given a DNS address
  It calls upon the local host to resolve the address
  This can be done in variety of ways:
    Table look up
      On UNIX hosts: /etc/hosts
    Process communicates with a local name servers
      named on a UNIX system
    By sending a massage to the remote system that is identified from the information in the file /etc/resolv.conf

## Slide 33: Caching
When a name server receives a query for a domain that is does not serve
  It may send back a referral to the client by specifying better name servers
  It also may operate in a recursive manner
    Any DNS server passes requests it cannot handle to higher level server and so on, until either the request can be handled or until the root of the DNS name space is reached

## Slide 34: Caching
Name servers contain pointers to other name servers with the help of which it is possible to traverse the entire domain naming hierarchy
  A host with the initial name server addresses has to be configured
  After this, it is able to use DNS protocols to locate the name server responsible for any part or the DNS naming hierarchy

## Slide 35: Caching
When a name server receives a request, it can do one of the following:
  Answer the request with an IP address
    Iterative method
      Client simply asks the server to resolve a domain name
      Server accesses its database
        Address found
          Address sent back
        Address not found
          Sends back an error “DNS not found”
  Contact another name server and try to find the IP address for the requested name
    Send back a referral to the client specifying the IP address of better name servers

## Slide 36: Caching
A popular user interface - 'nslookup'
  Available on the UNIX systems
  Can perform any DNS function
  Also displays the result to the user
Using nslookup
  Can obtain a listing of all the hosts in a zone
  To do this, first need to identify the nameserver for the zone

## Slide 37: Exposures

## Slide 38: Threats
Lack of integrity and authenticity checking of the data held within the DNS
Other protocols can use host names as an access control mechanism
  Internet engineering task force (IETF) has come up with DNS security (DNSSEC) extensions to DNS protocol
    Main objective is to provide authentication and integrity to the DNS
    Provided through the use of cryptographic

## Slide 39: DNS is required for the Internet to work
Yes
No