## Slide 1: Firewalls

## Slide 2: Reading
Computer Networking Illuminated
  Chapter 10.4 - Firewalls
Linux Administration: A beginners Guide
  Linux Firewall
    329-355
    Concentrate on the Firewall part

## Slide 3: Firewalls
Network layer firewall
  Works as a packet filter
  Decides what packets will pass the firewall
    According to rules
      Defined by an administrator
    Filtering rules can act on the basis of:
      source address
      destination address
      ports
      higher-level network protocols the packet contains
      time of day
      and more…
Network layer firewalls:
  Tend to operate very fast
  Transparent to users

## Slide 4: Network layer firewalls
Generally fall into two sub-categories
  Non-stateful (stateless)
    Have packet-filtering capabilities
    Cannot make more complex decisions on what stage communications between hosts have reached
    Offer less security
    Somewhat resemble a router in their ability to filter packets
  Stateful
    Hold some information on the state of connections as part of their rules
      For example:
        established or not, initiation, handshaking, data or breaking down the connection
        only hosts inside the firewall can establish connections on a certain port

## Slide 5: Firewalls
Can be:
  Software implementation
    Extra software on the host
      Any computer running an operating system that supports packet filtering and routing can function as a network layer firewall
      Appropriate operating systems for such a configuration include Linux, Solaris, BSDs or Windows Server
  Hardware implementation
    An external device (computer) with special software
Typically:
  Combination of Hardware devices and Software

## Slide 6: Stateless Firewalls

## Slide 7: Stateless Firewall
Firewall that treats each network frame (or packet) in isolation
  It has no way of knowing if any given packet is:
    Part of an existing connection
    Trying to establish a new connection
    Rogue packet
Typical behavior of firewalls before the advent of stateful firewalls
  Modern firewalls are connection-aware (or state-aware)
  Allows network administrators finer-grained control of network traffic

## Slide 8: Stateless Firewalls
Problem:
  Classic example is the File Transfer Protocol (FTP)
    By design FTP opens new connections to random ports
  Suppose you are the firewall of Company X, protecting the company from unauthorized traffic from the Internet
    You notice a TCP packet coming from some host across the globe, destined for a machine of your internal network, TCP port number 4970
    This port number does not correspond to any well-known service that your protected network is supposed to provide (like Web, FTP or SSH)
      Discard the packet
      Just broke a legitimate FTP connection!

## Slide 9: Stateless Firewalls
FTP (among other protocols)
  Needs to be able to open connections to arbitrary high ports to function properly
  E.g. a host's port 4970
Firewall has no way of knowing that the packet destined to the protected network is part of a legitimate FTP session
  Drops the packet
Stateful firewalls solve this problem
  Maintains a table of open connections
  Intelligently associates new connection requests with existing, legitimate connections

## Slide 10: Stateful Firewalls

## Slide 11: Stateful Firewalls
A firewall that keeps track of the state of network connections traveling across it
  such as TCP streams
Performs stateful packet inspection or stateful inspection
Programmed to distinguish legitimate packets for different types of connections
Only packets which match a known connection state will be allowed by the firewall
  Others will be rejected

## Slide 12: Stateful Firewalls
Early attempts at producing firewalls operated at the application level of the 7-layer OSI model
  Required too much CPU power
Packet filters operate at the network layer (layer-3)
  Function more efficiently because they only look at the header part of a packet
However, pure packet filters
  Have no concept of state
  Subject to spoofing attacks and other exploits

## Slide 13: Stateful Firewalls
How It Works
  Holds in memory significant attributes of each connection
    Start to finish
  Attributes, collectively known as the state of the connection, may include such details as:
    IP addresses and ports involved in the connection
    Sequence numbers of the packets traversing the connection
  Most CPU intensive checking is performed at the time of setup of the connection
    All packets after that (for that session) are processed rapidly
      Simple and fast to determine whether it belongs to an existing, pre-screened session
  Once the session ends, entry in the state-table is discarded

## Slide 14: Stateful Firewalls
How It Works…
  Depends on the three-way handshake of the TCP protocol
    When a client initiates a new connection, it sends a packet with the SYN bit set in the packet header.
    All packets with the SYN bit set are considered by the firewall as NEW connections.
    If the service which the client has requested is available on the server
      Service will reply to the SYN packet with a packet in which both the SYN and the ACK bit are set.
    Client will then respond with a packet in which only the ACK bit is set
      Connection will enter the ESTABLISHED state.
  Firewall built-in to Windows XP will:
    Pass all outgoing packets through
    Only allow incoming packets if they are part of an ESTABLISHED connection
    Ensure hackers cannot start unsolicited connections with the protected machine

## Slide 15: Stateful Firewalls
How it Works (cont)
  In order to prevent the state table from filling up
    Sessions will time out if no traffic has passed for a certain period
    Stale connections are removed from the state table
    Many applications therefore send keepalive messages periodically
      Keeps a firewall from dropping the connection during periods of no user-activity
      Some firewalls can be instructed to send these messages for applications
  It is worth noting that the most common Denial of Service attack on the internet these days is the SYN flood
    A malicious user intentionally sends large amounts of SYN packets to the server in order to overflow its state table
    Blocks the server from accepting other connections

## Slide 16: Stateful Firewalls
How it Works (cont)
  Many stateful firewalls are able to track the state of connections in connectionless protocols, like UDP
    Such connections usually enter the ESTABLISHED state immediately after the first packet is seen by the firewall
    Sessions in connectionless protocols can only end by time-out
  By keeping track of the connection state stateful firewalls provide added efficiency in terms of packet inspection
    Existing connections: firewall need only check the state table
      instead of checking the packet against the FW's rule set
      can be extensive
    An additional cost when the firewall’s rule set is updated
      Should cause the state table to be flushed
    The concept of deep packet inspection is unrelated to stateful firewalls

## Slide 17: Stateful Firewalls
Application-level Filters
  Today, firewalls are again using application level filters called proxies - or application level proxies
    Machines with modern CPU speeds can do deep packet inspection
    These proxies can read the data part of each packet
      Make a more intelligent decision about the connection
  For IRC or peer to peer file sharing protocols
    Traditional stateful firewalls cannot detect this
    An application level firewall can detect and selectively block HTTP connections according to content
  Modern computers typically exchange data by breaking it up to network frames
    “Packets" in TCP/IP
    Firewalls inspect each packet and decide:
      Should be allowed to pass the firewall and continue travelling towards its destination
      Should it be discarded
    Common ways of filtering packets are according to the source/destination address or according to the source/destination port

## Slide 18: Stateful Firewalls
Application-level Filters
  But in some cases this information is not enough.
    The administrator of the firewall might want to allow packets to pass the firewall according to the context of the connection, and not just the packet header characteristics.
    This deep packet inspection provides a much finer grained control
  Deep packet inspection costs more time to process, thus it is important to compensate for this by also providing stateful inspection
    Note: The finer-grained security functionality provided by application-level filters can be defeated by users who encrypt packet contents (e.g. by tunneling via SSL)

## Slide 19: Stateful Firewalls
Examples of stateful firewalls:
  VPN-1/FireWall-1
  Cisco PIX
  IPFilter
  Netfilter
    kernel-level packet filter of the Linux kernel.
  PF, OpenBSD packet filter, also found in other BSDs
Examples of application level proxy firewalls:
  Sidewinder G2 (Secure Computing)
    a hybrid of the earlier SC Sidewinder and NAI Gauntlet firewalls
    closer now to Gauntlet than the old Sidewinder
  Cyberguard (Now owned by Secure Computing)
  Gauntlet
  Symantec Enterprise Firewall

## Slide 20: Firewalls:
Block unwanted traffic
Pass permitted traffic
Can block specific protocols
Can block by time of day
All of the above
10
30 sec

## Slide 21: Firewall Summary
Firewalls
  Simply filter out unwanted traffic
  Can have complex rules
  Simplest ones allow only return communications from sessions established by the host computer
  Firewall hardware may have extra features
    Can mask the real IP address of computers behind it via NAT
    Many support DHCP

## Slide 22: Router vs. Firewall
Both:
  Examine data presented a NIC
  Have rules to handle the data
Routers:
  Pass data to where it is needed
  Ignore otherwise
Firewalls:
  Data is trying to pass to a destination
  Block data that is not wanted