## Slide 1: NAT
Network Address Translation

## Slide 2: Reading
CNI – pp. 251-253
  Port Mapping
LA – pp. 331-335
  NAT

## Slide 3: Network Address Translation

## Slide 4: Network Address Translation
Gateway and firewall hardware often has Network Address Translation (NAT) functionality built in
    Hosts protected behind a firewall commonly have addresses in the "private address range“
    Hides the true address of protected hosts
    Originally, developed to address the limited amount of IPv4 routable addresses available
      By companies
      By individuals
    Reduce amounts of addresses required
      Reduce the cost of obtaining enough public addresses for every computer in an organization.
    Hiding the addresses of protected devices has become an increasingly important defense against network reconnaissance

## Slide 5: Nat Flavors
Two kinds of network address translation:
  Simple "NAT"
      also sometimes named "Network Address Port Translation" or "NAPT" or even PAT
    Involves the mapping of port numbers
    Allows multiple machines to share a single IP address
      Typically used in home environments
TCP Header Format
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Source Port | Destination Port |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Acknowledgment Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Data | |U|A|P|R|S|F| |
| Offset| Reserved |R|C|S|S|Y|I| Window |
| | |G|K|H|T|N|N| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Checksum | Urgent Pointer |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Options | Padding |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| data |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 6: Nat Flavors
Two kinds of network address translation:
  “Other” NAT
      "one-to-one NAT" or "basic NAT" or “static NAT”
    Involves only address translation, not port mapping
    Requires a unique external IP address for each simultaneous connection
    Broadband routers often use this feature
        Sometimes labeled "DMZ host“
      Allows a designated computer to accept all external connections even when the router itself uses the only available external IP address
  Example
    50 hosts in the LAN
      All with Local addresses
    10 IP addresses for the Internet
    Up to 10 of the LAN hosts can access the internet through the Internet IP addresses

## Slide 7: NATP
NAT with port-translation comes in two sub-types:
  Source address translation (source NAT)
    Outgoing packets
    Re-writes the IP address of the computer which initiated the connection
  Destination address translation (destination NAT)
    Incoming packets
In practice
  Both are usually used together in coordination for two-way communication

## Slide 8: NAT Summary
Allows private addresses access to internet
Allows many addresses to share
  A single address
  A small set of addresses