## Slide 1: VPN
http://en.wikipedia.org/wiki/Vpn

## Slide 2: VPN
Virtual private network

## Slide 3: VPN
Intro

## Slide 4: Virtual Private Network (VPN)
Typically operates at the WAN Level
  Often across the public internet
Communications network tunneled through another network and dedicated for a specific network
  Commonly used for secure communications via the public Internet
  VPN need not have explicit security features
    Authentication or content encryption
  VPNs can be used to separate the traffic of different user communities
    Underlying network with strong security features

## Slide 5: Virtual Private Network (VPN)
VPNs may have different priorities
  Best-effort performance
  A defined Service Level Agreement (SLA)
  Whatever is important between the VPN customer and the VPN service provider
Generally, a VPN has a topology more complex than point-to-point
The distinguishing characteristic of VPNs:
  Based on Administrative relationships
    Not on security or performance
  Overlay other network(s)
    Provides a functionality that is meaningful to a user community

## Slide 6: Concepts
Tunneling
http://en.wikipedia.org/wiki/Tunneling_protocol

## Slide 7: Tunneling protocol
Tunneling protocol:
  A network protocol which encapsulates a payload protocol
  Reasons to tunnel include:
    Carry a payload over an incompatible delivery network
    Provide a secure path through an untrusted network

## Slide 8: Tunneling protocol
Tunneling
  Does not always fit a layered protocol model such as those of OSI or TCP/IP
  To understand a particular protocol stack
    Both the payload and delivery protocol sets must be understood
Note: Protocol encapsulation that is carried out by conventional layered protocols is not considered tunneling
  E.g. HTTP over TCP over IP over PPP over a V.92 modem

## Slide 9: Tunneling protocol
IP payload might believe it sees a data link layer delivery when it is carried inside the Layer 2 Tunneling Protocol (L2TP)
  Appears to the payload mechanism as a protocol of the data link layer
  L2TP, however, actually runs over the transport layer using User Datagram Protocol (UDP) over IP
The IP in the delivery protocol could run over any data link protocol from IEEE 802.2 over IEEE 802.3 (i.e., standards-based Ethernet) to the Point-to-Point Protocol (PPP) over a dialup modem link

## Slide 10: Tunneling protocol
Tunneling protocols may use data encryption to transport
  Protect normally insecure payload protocols
  Over a public network such as the Internet
  Providing VPN functionality
IPSec has an end-to-end Transport Mode
  Can operate in a Tunneling Mode through a trusted security gateway

## Slide 11: SSH tunneling
SSH is frequently used to tunnel insecure traffic over the Internet in a secure way
  Windows machines can share files using the SMB protocol
    by default, NOT encrypted
  If a Windows file system is mounted remotely through the Internet
    Someone snooping on the connection could see your files
To mount an SMB (Server Message Block) file system securely
  Establish an SSH tunnel
    Route all SMB traffic to the fileserver inside an SSH-encrypted connection
  SMB traffic itself is insecure
    Travelling within an encrypted connection makes it secure

## Slide 12: Tunneling to circumvent firewall policy
Tunneling can also be used to traverse a firewall (firewall policy permitting that protocol)
  Protocols that are normally blocked by the firewall
    Encapsulated inside a commonly allowed protocol such as HTTP or DNS
  If the policy on the firewall does not exercise enough control over HTTP requests, this can sometimes be used to circumvent the intended firewall policy

## Slide 13: Tunneling to circumvent firewall policy
Another HTTP-based tunneling method uses the HTTP CONNECT method/command
  Command tells an HTTP proxy to make a TCP connection to the specified server:port
  Relay data back and forth between that connection and the client connection
  For security reasons CONNECT-capable HTTP proxies commonly restrict access to the CONNECT method to accessing TLS/SSL-based HTTPS services only

## Slide 14: Common tunneling protocols
Examples of tunneling protocols include:
  Datagram-based:
    IPsec
    GRE (Generic Routing Encapsulation)
    IP in IP Tunneling
    L2TP (Layer 2 Tunneling Protocol) [2]
    MPLS (Multi-Protocol Label Switching)
    GTP (GPRS Tunnelling Protocol)
    PPTP (Point-to-Point Tunneling Protocol) [3]
    PPPoE (point-to-point protocol over Ethernet)
    PPPoA (point-to-point protocol over ATM)
    IEEE 802.1Q (Ethernet VLANs)
    DLSw (SNA over IP)
    XOT (X.25 datagrams over TCP)
    IPv6 tunneling: 6to4; 6in4; Teredo
    Anything In Anything (AYIYA; e.g. IPv6 over UDP over IPv4, IPv4 over IPv6, etc.)
  Stream-based:
    TLS
    SSH
    SOCKS
    HTTP CONNECT command
    Various Circuit-level proxy protocols
      MS Proxy server's Winsock Redirection Protocol
      WinGate Winsock Redirection Service.

## Slide 15: Business Case for Using VPN

## Slide 16: Business Case for VPN
Attractions of VPNs to enterprises include:
  Shared facilities may be cheaper than traditional routed networks over dedicated facilities
    especially in capital expenditure ($$$$$)
  Can rapidly link enterprise offices
    Also small-and-home-office and mobile workers
  Allow customization of security and quality of service as needed for specific applications
    Especially when provider-provisioned on shared infrastructure, can scale to meet sudden demands
  Reduce operational expenditure ($$$$$)
    Outsourcing support and facilities

## Slide 17: Business Case for VPN
Distributing VPNs to homes, telecommuters, and small offices
  May put access to sensitive information in facilities not as well protected as more traditional facilities
VPNs need to be designed and operated with well-thought-out security policies
Organizations using VPNs must have clear security rules supported by top management
When access goes beyond traditional office facilities
  Security must be maintained as transparently as possible to end users
  Especially where there are no professional administrators

## Slide 18: Business Case for VPN
Example to handle Sensitive Data:
  Arrange for an employee's home to have two separate WAN connections:
    One for working on that employer's sensitive data
    One for all other uses (private use)
  Bringing up the secure VPN cuts off all other Internet connectivity
    Only secure communications into the enterprise allowed
    Internet access is still possible
      Will go through enterprise access rather than that of the local user

## Slide 19: Business Case for VPN
Where a company or individual has legal obligations to keep information confidential, there may be legal problems, even criminal ones
Examples:
  HIPAA regulations in the U.S. with regard to health data
  General European Union data privacy regulations
    Apply to even marketing and billing information
    Extend to those who share that data elsewhere

## Slide 20: Categorizing VPNs: User Administrative Relationships

## Slide 21: Categorizing VPNs
IETF has categorized a variety of VPNs
  Other organizations may have definitions also:
    Institute of Electrical and Electronics Engineers (IEEE) Project 802, Workgroup 802.1 (architecture)
    Virtual LANs (VLAN)

## Slide 22: Categorizing VPNs
Originally, network nodes within a single enterprise were interconnected with Wide Area Network (WAN) links from a telecommunications service provider
  With the advent of LANs, enterprises could interconnect their nodes with links that they owned
  Original WANs used dedicated lines and layer 2 multiplexed services such as Frame Relay
  IP-based layer 3 networks became common interconnection media
    ARPANET
    Internet
    Military IP networks (NIPRNET,SIPRNET,JWICS, etc.)
VPNs began to be defined over IP networks
Military networks may themselves be implemented as VPNs on common transmission equipment
  With separate encryption and perhaps routers

## Slide 23: Categorizing VPNs
Distinguish among different kinds of IP VPN interconnecting the nodes
  Based on the administrative relationships
  Not the technology
Once the relationships are defined
  Different technologies could be used
  Depending on requirements:
    Security
    Quality of service

## Slide 24: Categorizing VPNs
Intranet
  An enterprise interconnected set of nodes
  All under its administrative control
    Through an IP network
Extranet
  Interconnected nodes under multiple administrative authorities
  Hidden from the public Internet
Both intranets and extranets:
  Could be managed by a user organization
  Service could be obtained as a contracted offering
    Usually customized, from an IP service provider
For an IP service provider:
  User organization contracted for layer 3 services
    Like it had contracted for layer 1 services
      Dedicated lines
      Multiplexed layer 2 services such as frame relay

## Slide 25: Categorizing VPNs
IETF distinguishes between VPN parts:
  Provider-provisioned
  Customer-provisioned
Conventional WAN services can be provided by an interconnected set of providers
  Provider-provisioned VPNs (PPVPNs) can be provided by a single service provider that presents a common point of contact to the user organization

## Slide 26: VPNs and Routing

## Slide 27: VPNs and Routing
Tunneling protocols can be used in a point-to-point topology that would generally not be considered a VPN
  VPN is accepted to support arbitrary and changing sets of network nodes
Most router implementations support software-defined tunnel interface
  Customer-provisioned VPNs are often simply a set of tunnels over which conventional routing protocols run
PPVPNs need to support the coexistence of multiple VPNs
  Hidden from one another
  Operated by the same service provider

## Slide 28: Building Blocks
Depending on whether the PPVPN is layer 2 or layer 3
  The building blocks may be
    L2 only (hardware/NIC addressing, e.g. MACs)
    L3 only (network/IP addressing)
    Combinations of the two
  MPLS functionality blurs the L2-L3 identity
    (Multi-Protocol Layer Switching)
Basic Blocks
  Customer Edge Device
  Provider Edge Device
  Provider Device

## Slide 29: Customer Edge Device (CE)
A CE is a device that provides access to the PPVPN service
  Physically at the customer premises
Some implementations treat it purely as a demarcation point between provider and customer responsibility
  Others allow it to be a customer-configurable device

## Slide 30: Provider Edge Device (PE)
A PE is a device or set of devices which supplies the provider's view of the customer site
  At the edge of the provider network
PEs are aware of the VPNs that connect through them
  Do maintain VPN state

## Slide 31: Provider Device (P)
A P Device does not directly interface to any customer endpoint
  Inside the provider's core network
  Might be used to provide routing for many provider-operated tunnels that belong to different customers' PPVPNs
P device is a key part of implementing PPVPNs
  It is not itself VPN-aware and does not maintain VPN state
Principal role is allowing the service provider to scale its PPVPN offerings
  For example, by acting as an aggregation point for multiple PEs
P-to-P connections are often high-capacity optical links between major locations of provider

## Slide 32: User-Visible PPVPN Services (Provider Provisioned VPN)
Types of VPN currently considered active in the IETF

## Slide 33: OSI – Quick Reminder
OSI Model
  Open Systems Interconnection
  7 layers to define communications
  We need only be concerned with the first 4 or 5 layers at the infrastructure level

## Slide 34: Layer 1 Services
Virtual Private Wire (VPWS) and Virtual Private Line Services (VPLS)
  Provider does not offer a full routed or bridged network
    Components from which the customer can build customer-administered networks
      VPWS are point-to-point
      VPLS can be point-to-multipoint
    Can be Layer 1 emulated circuits with no data link structure
  Customer determines the overall customer VPN service
    Can involve routing, bridging, or host network element
  Acronym collision between
    Virtual Private Line Service
    Virtual Private LAN Service
    Context should make it clear which is meant
      Layer 1 virtual private line
      Layer 2 virtual private LAN

## Slide 35: Layer 2 Services
Virtual LAN
  Layer 2 technique that allows for the coexistence of multiple LAN broadcast domains
    Interconnected via trunks using the IEEE 802.1Q trunking protocol.
  Other trunking protocols have been used but are obsolete
    Inter-Switch Link (ISL)
    IEEE 802.10
    ATM LAN Emulation (LANE)

## Slide 36: Layer 2 Services
Virtual Private LAN Service (VPLS)
  VLANs allow multiple tagged LANs to share common trunking
    Frequently are composed only of customer-owned facilities
    Layer 1 technology that supports emulation
      point-to-point
      point-to-multipoint topologies
  VPLS is a Layer 2 PPVPN
    Emulates the full functionality of a traditional LAN
    From the user standpoint
      Makes it possible to interconnect several LAN segments over a packet-switched or optical provider core
      Makes the remote LAN segments behave as one single LAN
    Provider network emulates a learning bridge
      May optionally include VLAN service

## Slide 37: Layer 2 Services
Pseudo Wire (PW)
  PW is similar to VPWS
    Provide different L2 protocols at both ends
    Interface is a WAN protocol such as ATM or Frame Relay
    When the goal is to provide the appearance of a LAN contiguous between two or more location
      Virtual Private LAN service or IPLS would be appropriate
IP-Only LAN-Like Service (IPLS)
  A subset of VPLS, the CE devices must have L3 capabilities
    IPLS presents packets rather than frames
    May support IPv4 or IPv6

## Slide 38: Layer 3
L3 PPVPN Architectures
  In one architecture the PE disambiguates duplicate addresses in a single routing instance
    BGP/MPLS PPVPN
  In the other architecture (virtual router) the PE contains a virtual router instance per VPN
  One of the challenges of PPVPNs is that different customers may use the same address space
    especially the IPv4 private address space
      e.g. both used the 192.168.1.0 address space
    provider must be able to disambiguate overlapping addresses in the multiple customers' PPVPNs

## Slide 39: Layer 3
Virtual Router PPVPN
  The Virtual Router architecture requires no modification to existing routing protocols
    By the provisioning of logically independent routing domains
      Customer operating a VPN is completely responsible for the address space
    In the various MPLS tunnels, the different PPVPNs are disambiguated by their label, but do not need routing distinguishers
  Virtual router architectures do not need to disambiguate addresses
    PE contains multiple virtual router instances
      which belong to one and only one VPN

## Slide 40: Categorizing VPN Security Models

## Slide 41: VPN Security Models
From the security standpoint
  either the underlying delivery network is trusted
  or the VPN must enforce security with mechanisms in the VPN itself
Unless the trusted delivery network runs only among physically secure sites
  Both trusted and secure models need an authentication mechanism for users to gain access to the VPN

## Slide 42: VPN Security Models
Some ISPs offer managed VPN service for business customers
  Want the security and convenience of a VPN
  Prefer not to undertake administering a VPN server themselves
Managed VPNs go beyond PPVPN scope
  Contracted security solution that can reach into hosts
  Provide remote workers with secure access to their employer's internal network
  Other security and management services sometimes included as part of the package
Examples include keeping anti-virus and anti-spyware programs updated on each client's computer

## Slide 43: VPN Security Models
Authentication before VPN Connection
  A known trusted user can be provided with appropriate security privileges to access resources not available to general users
    Servers may also need to authenticate themselves to join the VPN
  Wide variety of authentication mechanisms
    May be implemented in devices
      Firewalls
      Access gateways
      Other devices
    May use passwords, biometrics, or cryptographic methods
    Strong
      Involves using at least two authentication mechanisms
    Authentication mechanism may:
      Require explicit user action
      Be embedded in the VPN client or the workstation

## Slide 44: Trusted Delivery Networks
Trusted VPNs do not use cryptographic tunneling
  Rely on the security of a single provider's network
  Elaboration of traditional network and system administration work
    Sometimes referred to APNs - Actual Private Networks
Multi-Protocol Label Switching (MPLS)
  Often used to overlay VPNs
    Often with quality of service control over a trusted delivery network
Layer 2 Tunneling Protocol (L2TP)
  Standards-based replacement
  Compromise taking the good features from each, for two proprietary VPN protocols:
    Cisco's Layer 2 Forwarding (L2F) (now obsolete)
    Microsoft's Point-to-Point Tunneling Protocol (PPTP)

## Slide 45: Security mechanisms in the VPN
To achieve privacy
  Secure VPNs use cryptographic tunneling protocols to provide:
    Intended confidentiality
      blocking snooping and Packet sniffing
    Sender authentication
      blocking identity spoofing
    Message integrity
      blocking message alteration
One gets secure communications over unsecured networks when the proper techniques are:
  Chosen
  Implemented
  Used

## Slide 46: Security mechanisms in the VPN
Secure VPN protocols include the following:
  IPsec (IP security)
    commonly used over IPv4, and an obligatory part of IPv6
  SSL/TLS
    Used either for tunneling the entire network stack or for securing web proxy
    SSL is a framework more often associated with e-commerce
      Has been built-upon by a number of vendors to provide remote access VPN capabilities
  OpenVPN
    Variation of SSL-based VPN that
    Capable of running over UDP
  VPN Quarantine
    Client machine at the end of a VPN could be a threat and a source of attack
    No connection with VPN design and is usually left to system administration efforts
    Solutions available that provide VPN Quarantine services
      Run end point checks on the remote client
      Client is kept in a quarantine zone until healthy