## Slide 1: ARP
Address Resolution Protocol
Ref: http://en.wikipedia.org/wiki/Address_Resolution_Protocol

## Slide 2: Preliminary
Network and Broadcast Addresses

## Slide 3: Network and Broadcast Address
Network Address
  First “address” in a network or subnet
    A.K.A. wire address
  Not a valid host ID
  All 0s for the network or subnet host id
    192.168.001.000
    172.016.000.000
    010.000.000.000
  Useful when describing a subnet
    172.016.004.000/24
      Class C network subdivided into Class C sizes
      172.16.4.0 – 172.16.4.255 in this case
    192.168.001.000/25
      .000  0000 0000
      Subnet of the first 128 addresses in 192.168.1.x
        Hosts 192.168.1.1 – 192.168.1.126
    192.168.001.128/25
      .128  1000 000
      Subnet of the last 128 addresses in 192.168.1.x
        Hosts 192.168.1.129 – 192.168.1.254

## Slide 4: Network and Broadcast Address
  Broadcast address
  Last “address” in a network or subnet
    Everyone in the network is to listen to this message
  Not a valid host ID
  All 1s for the network or subnet host id
    172.017.255.255
    010.255.255.255
    192.168.005.127/25
      .127  0111 1111
      Broadcast address for the 192.168.5.0/25 subnet
      All in the range 192.168.5.1-192.168.5.126
    192.168.005.255/25
      .255  1111 1111
      Broadcast address for the 192.168.5.128/25 subnet
      All in the range 192.168.5.129-192.168.5.254

## Slide 5: MAC Side Note
MAC’s have a broadcast address:
  ff:ff:ff:ff:ff:ff
  Everybody listen

## Slide 6: ARP

## Slide 7: Problem
Hosts can only communicate Host to nearby Host
  This means MAC address to MAC address
  These machines must be on the same connected physical (local) network
    On the same Hub or Switch
Programs typically want to communicate with programs on other machines on other networks
  Whether or not they are on the same network
  Specifically, working at the IP address level
How do programs get their messages to the other machines?
ARP is one critical key in the solution
  One machine can request the MAC address of a machine with a specific IP address

## Slide 8: ARP
Address Resolution Protocol
  Method for finding a host's hardware address (MAC) when only its network layer address (IP) is known
    Remember OSI layers?
ARP is defined in RFC 826.
  Current Internet Standard: STD 37

## Slide 9: ARP
Not an IP-only or Ethernet-only protocol
  Can be used to resolve many different network-layer protocol addresses to hardware addresses
However:
  Nowadays almost all traffic is IPv4 and Ethernet
    IPv6 is up and coming!
    Primarily used to translate IP addresses to Ethernet MAC addresses
    Also used for IP over other LAN technologies
      Token Ring, FDDI, or IEEE 802.11
      IP over ATM

## Slide 10: ARP
IPv6
  ARP's functionality is provided by the Neighbor Discovery Protocol (NDP)

## Slide 11: Basic Steps
Need to send a message to a specific IP:
  Is the desired IP address in local ARP cache?
    Yes – done
      Use the noted MAC address for this IP address
    No – broadcast “Who is IP w.x.y.z?”
      Host with that IP address responds
        Returns its IP address and MAC address
        Requester saves info in its cache
        Uses the MAC address to send message
      No response?
        Give up

## Slide 12: Examples

## Slide 13: Sample Network
R1
A
B
D
R2
R3
C
Switch
Router
A
Host
More
network
More
network
More
network

## Slide 14: Examples
ARP is used in four cases of two hosts communicating:
  Two hosts are on the same network (A B)
    One desires to send a packet to the other
  Two hosts are on different networks (A  C)
    Must use a gateway/router to reach the other host
    Gets packet out of the originating network
  Router needs to forward a packet (R1  R2)
    From router to router
    Gets it one step closer to the destination network
  Router needs to forward a packet (R3  D)
    From end router to the destination host on the same network
    Gets it to the destination network
Notes:
  Cases 1 and 2 the hosts are primary players
  Cases 3 and 4 are really subcases of 2
    The routers, which are hosts, are intermediaries

## Slide 15: Examples
First case is used when two hosts are on the same physical network
  They can directly communicate without going through a router
  Note: the hosts also must be on the same logical network
Last three cases
  Mostly used over a Network or the Internet
    Two computers on the Internet are typically separated by more than 3 hops
  Note: the hosts are usually on different logical networks

## Slide 16: First Case
Two hosts, A and B, on the same LAN segment
  Host A wants to send an IPv4 packet to Host B
    Host A must know the IPv4 address for Host B
  To send the packet on the LAN to Host B
    Host A must also have a Link Layer address
      E.g. the MAC address for Host B
  If MAC address is unknown
    Send an ARP request
      MAC Broadcast: Who has a MAC address for this IP address?
        All the MACt bits are set to 1 (broadcast address), e.g.:
          ff:ff:ff:ff:ff:ff
      All NICs see broadcast messages
        All hosts pay attention to their logical network messages
    Wait for a reply
      From Host B or another device on the network
        Returning a MAC address

## Slide 17: Second Case
Like Case 1: but Hosts would be on different network segments (A  R  C)
  Router on the same LAN segment as Host A
    Either
      On the same network segment as Host C
      On the same network segment as another router
        That is on the same network segment as Host C
      On the same network segment as another router
        That is on the same network segment as another router
          That is on the same segment as Host
      And so on …
  Host A would not send the IPv4 packet directly to Host C
    But to the first of those routers
      It would look up Host C in its routing table to determine the IPv4 address of the appropriate router
  Use ARP to determine that MAC address of the router
    If it doesn't already know the MAC address for that router

## Slide 18: Third and Fourth Cases
Third case similar to the second case (Rx  Ry)
  Router would look up Host D in its routing table to determine the IPv4 address of the next router to which it should send the packet
    R1  R2 or R2  R3
  If it doesn't already know the MAC address for the router, use ARP to determine that MAC address
Fourth case similar to the first case (Rx  D)
  Router has determined that Host D is on the same LAN segment
  If it doesn't already know Host B's MAC address, will use ARP to determine that MAC address

## Slide 19: ARP mediation
Process of resolving Layer 2 addresses when different resolution protocols are used on either circuit
  E.g. ATM on one end and Ethernet on the other

## Slide 20: Inverse ARP
Inverse Address Resolution Protocol (InARP)
  Protocol used for obtaining Layer 3 addresses (e.g. IP addresses) of other stations from Layer 2 addresses (e.g. MAC addresses)
  Primarily used in Frame Relay and ATM networks
    Layer 2 addresses of virtual circuits are sometimes obtained from Layer 2 signaling
    Corresponding Layer 3 addresses must be available before these virtual circuits can be used.
ARP translates Layer 3 addresses to Layer 2 addresses
  InARP can be viewed as its inverse
  InARP is actually implemented as an extension to ARP
  The packet formats are the same
    Only the operation code and the filled fields differ

## Slide 21: Resume 2/1

## Slide 22: ARP Packet structure
Above is the packet structure used for ARP requests and replies
HTYPE: Ethernet = 1
PTYPE: IPv4 = 0x0800
  On Ethernet networks, these packets use an
    EtherType of 0x0806 – IPv4 ARP
    Sent to the broadcast MAC address of FF:FF:FF:FF:FF:FF
Note that the packet structure example shown in the table has SHA, SPA, THA, & TPA as 32-bit words
  Actual lengths determined by the hardware & protocol length fields
+ | Bits 0 - 7 | 8 - 15 | 16 - 31
0 | Hardware type (HTYPE) |  | Protocol type (PTYPE)
32 | Hardware length (HLEN) | Protocol length (PLEN) | Operation (OPER)
64 | Sender hardware address (SHA) |  | 
? | Sender protocol address (SPA) |  | 
? | Target hardware address (THA) |  | 
? | Target protocol address (TPA) |  | 

## Slide 23: Packet structure
Field definitions:
  Hardware type (HTYPE)
    Each data link layer protocol is assigned a number used in this field
    For example, Ethernet is 1
  Protocol type (PTYPE)
    Each protocol is assigned a number used in this field
    For example, IPv4 is 0x0800
  Hardware length (HLEN)
    Length in bytes of a hardware address
    Ethernet addresses (MAC) are 6 bytes long
  Protocol length (PLEN)
    Length in bytes of a logical address
    IPv4 address are 4 bytes long
  Operation
    Specifies the operation the sender is performing:
      1 for request
      2 for reply
  Sender hardware address (SHA)
    Hardware address of the sender
  Sender protocol address (SPA)
    Protocol address of the sender
  Target hardware address (THA)
    Hardware address of the intended receiver
    This field is ignored in requests (what it is searching for)
  Target protocol address (TPA)
    Protocol address of the intended receiver

## Slide 24: Example request
Host:
  IPv4 address of 10.10.10.123 (0A.0A.0A.7B in hex)
    32 bits
  MAC address of 00:09:58:D8:11:22
    48 bits
Wants to send a packet to another host
  IPv4 address at:10.10.10.140 (0A.0A.0A.8C in hex)
  MAC address unknown
Must send an ARP request to discover the address
Sample packet of what would be broadcast over the local network:
+ | Bits 0 - 7 | 8 - 15 | 16 - 31 | 
0 | Hardware type = 1 |  | Protocol type = 0x0800 | 
32 | Hardware length=6 | Protocol length=4 | Operation = 1 (request) | 
64 | SHA (first 32 of 48 bits) = 0x000958D8 |  |  | 
96 | SHA (last 16 of 48 bits) = 0x1122 |  |  | SPA (first 16 of 32 bits) = 0x0A0A
128 | SPA (last 16 or 32 bits) = 0x0A7B |  |  | THA (first 16 of 48 bits) = 0xFFFF
160 | THA (last 32 of 48 bits) = 0xFFFFFFFF |  |  | 
192 | TPA (32 bits) = 0x0A0A0A8C |  |  | 

## Slide 25: Example reply
If the host 10.10.10.140 is running and available
  Notices the ARP request
  Send a reply packet as shown below
    Host 10.10.10.140 (0A.0A.0A.8C) has MAC address of 00:09:58:D8:33:AA
    Note that the sender and target address blocks are now swapped
      Sender of the reply is the target of the request
      The target of the reply is the sender of the request
    Host 10.10.10.140 has filled in its MAC address in the sender hardware address
+ | Bits 0 - 7 |  | 8 - 15 | 16 - 31 | 
0 | Hardware type = 1 |  |  | Protocol type = 0x0800 | 
32 | Hardware length=6 | Protocol length=4 |  | Operation = 2 (reply) | 
64 | SHA (first 32 of 48 bits) = 0x000958D8 |  |  |  | 
96 | SHA (last 16 of 48 bits) = 0x33AA |  |  |  | SPA (first 16 of 32 bits) = 0x0A0A
128 | SPA (last 16 of 32 bits) = 0x0A8C |  |  |  | THA (first 16 of 48 bits) = 0x0009
160 | THA (last 32 of 48 bits) = 0x58D81122 |  |  |  | 
192 | TPA (32 bits) = 0x0A0A0A7B |  |  |  | 

## Slide 26: ARP Announcements
AKA "Gratuitous ARP“
A packet (usually an ARP Request) containing
  Valid SHA and SPA for the host which sent it
  TPA = SPA
  THA = 0s –or– SHA
  Such a request is not intended to solicit a reply
    Other hosts which receive the packet update their ARP cache
Commonly done by many operating systems on startup
  Helps to resolve problems which might otherwise occur
    For example
      A network card had recently been changed
        Changing the IP-address-to-MAC-address mapping
      Some hosts still had the old mapping in their ARP caches
Other uses:
  Defend link-local IP addresses in the Zeroconf protocol
  IP address takeover within high-availability clusters

## Slide 27: ARP Probe
"IPv4 Address Conflict Detection" specification
  Is my address used by someone else?
Before beginning to use an IPv4 address
  No matter how assigned
    Manual configuration
    DHCP
    - or - some other means
  Host implementing an IPv4 address MUST test to see if the address is already in use
    broadcasting ARP probe packets
Details:
  SHA = senders real MAC address
  SPA = 0s (don’t use your IP address you’re checking)
  THA = 0s (really don’t care if there is no one)
  TPA = senders assumed IP address
  If you get a response someone is using your address

## Slide 28: ARP
Is used for TCP/IP only
Is platform dependent
Must have Ethernet to work
Is flexible in its hardware/software formats
1
30 sec

## Slide 29: Summary
ARP is used to find the hardware address (MAC) for a network protocol (IP) address
  Address of the target host if the host is on the local network
  Address of a router if the host is not on the local network
    Some router must know that it can forward it closer