## Slide 1: SNMP
Simple Network Management Protocol

## Slide 2: What is it?

## Slide 3: SNMP
Simple Network Management Protocol
  Part of the internet protocol suite
    Defined by the Internet Engineering Task Force (IETF)
  Used by network management systems
    Monitor network-attached devices for conditions that warrant administrative attention
    Manage said systems

## Slide 4: SNMP
Consists of a set of standards for network management
  Application Layer protocol
  Database schema
  Set of data objects

## Slide 5: SNMP
SNMP exposes management data
  Variables on the managed systems
  Describe the system configuration
Variables can be queried by managing applications
  Sometimes can be set

## Slide 6: Overview and basic concepts

## Slide 7: Overview and basic concepts
Typical SNMP environment:
  Large number of systems to be managed
  One or more systems manage them
An agent :
  Software component
  Runs on each managed system
  Reports information via SNMP to the managing systems

## Slide 8: Overview and basic concepts
SNMP agents reports data of interest on the managed systems
  Variables such as:
    "free memory“
    "system name“
    "number of running processes“
    "default route“
    “toner cartridge status”
    etc.

## Slide 9: Overview and basic concepts
Managing system can retrieve the information through protocol operations
  GET
  GETNEXT
  GETBULK
Agent can send data without being asked using protocol operations
  TRAP
  INFORM

## Slide 10: Overview and basic concepts
Management systems can
  Send configuration updates
  Send controlling requests
Uses the SET protocol operation to actively manage a system

## Slide 11: Overview and basic concepts
Configuration and control operations:
  Only used when changes are needed to the network infrastructure
Monitoring operations:
  Usually performed on a regular basis

## Slide 12: Overview and basic concepts
Variables accessible via SNMP are organized in hierarchies
Management Information Bases (MIBs)
  Contains the hierarchies and other metadata describing each variable’s
    type
    description

## Slide 13: Management Information Bases
MIBs

## Slide 14: Pre-Quiz: SNMP can
Monitor devices
Change devices
Warn of errors
All of the above
None of the above

## Slide 15: Management Information Bases
SNMP itself does not define which information (e.g. variables) a managed system should offer
SNMP uses an extensible design
  Available information defined by management information bases
    MIBs

## Slide 16: Management Information Bases
MIBs describe the structure of the management data of a device subsystem
  Use a hierarchical namespace containing object identifiers (OID)
  Each OID identifies a variable that can be read or set via SNMP
MIBs use a notation defined by ASN.1

## Slide 17: Management Information Bases
MIB hierarchy can be depicted as:
  A tree with a nameless root
  Levels which are assigned by different organizations
Top-level MIB OIDs belong to different standards organizations
Lower-level object IDs are allocated by associated organizations

## Slide 18: Management Information Bases
Model permits management across all layers of the OSI reference model
  Can extend into applications
    databases
    email
    Java EE reference model
    Etc.
  MIBs can be defined for area-specific information and operations

## Slide 19: Management Information Bases
A managed object1 is one of any number of specific characteristics of a managed device
  Managed objects comprise one or more object instances which are essentially variables
    Identified by their OIDs
1sometimes called an MIB object, an object, or a MIB

## Slide 20: Management Information Bases
Two types of managed objects exist:
  Scalar objects
    Define a single object instance
  Tabular objects
    Define multiple related object instances
    Grouped in MIB tables

## Slide 21: Management Information Bases
Example of a managed object
  atInput
    a scalar object that contains a single object instance
      An integer value
        Indicates the total number of input AppleTalk packets on a router interface
Object identifier (or object ID or OID)
  Uniquely identifies a managed object in the MIB hierarchy

## Slide 22: Examples
Resource:
  http://www.mibdepot.com/index.shtml
Example: 3Com device
  http://www.mibdepot.com/cgi-bin/xsearch_index3.cgi?id=173627
Example 2:
  http://www.oid-info.com/get/1.3.6.1.2.1

## Slide 23: From the top
example
  1.3.6.1.4.1.11
Start with the top level OID assignment
  http://www.alvestrand.no/objectid/top.html
    and work the way down

## Slide 24: ASN.1
Abstract Syntax Notation One

## Slide 25: Abstract Syntax Notation One (ASN.1)
Abstract Syntax Notation One (ASN.1)
  Standard and flexible notation
  Describes data structures for
    Representing
    Encoding
    Transmitting
    Decoding data
Provides a set of formal rules
  Describes the structure of objects
    Independent of machine-specific encoding techniques
    Precise, formal notation minimizes ambiguities

## Slide 26: Abstract Syntax Notation One (ASN.1)
Joint ISO and ITU-T standard
  Originally defined in 1984
    Part of CCITT X.409:1984
  Moved to its own standard, X.208 (1988)
    Due to wide applicability
  Substantially revised in 1995
    Covered by the X.680 series
Structure of Management Information (SMI)
  An adapted subset of ASN.1
  Specified in SNMP to define sets of related MIB objects
    Termed MIB modules.

## Slide 27: SNMP basic components

## Slide 28: SNMP basic components
SNMP-managed networks consist of three key components:
  Managed devices
  Agents
  Network-management systems (NMS)

## Slide 29: SNMP basic components
Managed device
  Network node that contains an SNMP agent
    Resides on a managed network
  Collect and store management information
    Make information available to NMSs using SNMP
Managed devices
  Sometimes called network elements

## Slide 30: SNMP basic components
Managed devices can be any type of device including, but not limited to:
  Routers and access servers
  Switches and bridges
  Hubs
  IP telephones
  Computer hosts
  Printers

## Slide 31: SNMP basic components
Agent
  Network-management software (NMS) module
    Executable program
    Resides in a managed device
  Has local knowledge of management information
    Translates that information into a form compatible with SNMP

## Slide 32: SNMP basic components
Network Management Systems
  Execute applications that monitor and control managed devices
  NMSs provide
    Bulk of the processing
    Memory resources required for network management
  One or more NMSs may exist on any managed network.

## Slide 33: SNMP architecture

## Slide 34: SNMP architecture
SNMP framework consists of
  Master agents
  Subagents
  Management stations

## Slide 35: Master agent
Software running on an SNMP-capable network component
  For example a router, that responds to SNMP requests from the management station
Acts as a:
  Server in client-server architecture terminology
  Daemon in operating system terminology
Relies on subagents to provide information about the management of specific functionality
Can also be referred to as managed objects

## Slide 36: Subagent
A piece of software running on an SNMP-capable network component
  Implements the information and management functionality defined by a specific MIB of a specific subsystem
    For example the ethernet link layer

## Slide 37: Subagent
Some capabilities of the subagent are:
  Gathering information from managed objects
  Configuring parameters of the managed objects
  Responding to managers' requests
  Generating alarms or traps

## Slide 38: Management station
Manager or management station
  Final component in the SNMP architecture
Functions as the equivalent of a client in the client-server architecture
  Issues requests for management operations
    On behalf of a administrator or application
  Receives traps from agents

## Slide 39: SNMP protocols

## Slide 40
SNMPv1 and SMI-specific data types

## Slide 41: SNMPv1 and SMI-specific data types
SNMPv1 SMI
  Specifies the use of a number of SMI-specific data types
Divided into two categories:
  Simple data types
  Application-wide data types
SMI – Structure of Management Information

## Slide 42: Simple data types
Three simple data types are defined in the SNMPv1 SMI:
  Integer data type:
    signed integer in the range of -231 to 231-1.
  Octet strings:
    ordered sequences of 0 to 65,535 octets
  Object IDs:
    From the set of all object identifiers allocated according to the rules specified in ASN.1
All are unique values

## Slide 43: Application-wide data types
Seven application-wide data types exist in the SNMPv1 SMI:
  Network addresses
  Counters
  Gauges
  Time ticks
  Opaques
  Integers
  Unsigned integers

## Slide 44: Application-wide data types
Network addresses
  Represent an address from a particular protocol family
  SNMPv1 supports only 32-bit IP addresses.
Counters
  Non-negative integers that increase
    Until they reach a maximum value
    Then return to zero
  In SNMPv1, a 32-bit counter size is specified

## Slide 45: Application-wide data types
Gauges
  Non-negative integers
    Can increase or decrease between specified minimum and maximum values
  A system property going outside the specified range:
    The value of the gauge itself will not go beyond the respective maximum or minimum
    Specified in RFC 2578.

## Slide 46: Application-wide data types
Time tick
  Represents a hundredth of a second since some event
Opaque
  Represents an arbitrary encoding that is used to pass arbitrary information strings that do not conform to the strict data typing used by the SMI

## Slide 47: Application-wide data types
Integer
  Represents signed integer-valued information
  Redefines the integer data type
    Arbitrary precision in ASN.1
    Bounded precision in the SMI
Unsigned integer
  Represents unsigned integer-valued information
  Useful when values are always non-negative
  This data type redefines the integer data type
    Arbitrary precision in ASN.1
    bounded precision in the SMI

## Slide 48: SNMPv1 MIB tables
SNMPv1 SMI defines highly structured tables
  Used to group instances of a tabular object
  Object that contains multiple variables
Tables are composed of zero or more rows
  Indexed in a way that allows SNMP to retrieve or alter an entire row with a single Get, GetNext, or Set command

## Slide 49
SNMPv2

## Slide 50: SNMPv2 and structure of management information
The SNMPv2 SMI is described in RFC 2578.
  It makes certain additions and enhancements to the SNMPv1 SMI-specific data types
    Including bit strings, network addresses, and counters
  Bit strings are defined only in SNMPv2
    Comprise zero or more named bits that specify a value
  Network addresses represent an address from a particular protocol family
  Counters are non-negative integers that increase until they reach a maximum value and then return to zero
    SNMPv1: a 32-bit counter size is specified
    SNMPv2: 32-bit and 64-bit counters are defined

## Slide 51: SNMPv2 and structure of management information
The SNMP protocol operates at the application layer (layer 7) of the OSI model.
Specifies (in version 1) five core protocol data units (PDUs):
  GET REQUEST
    Retrieve a piece of management information.
  GETNEXT REQUEST
    Iteratively to retrieve sequences of management information.
  GET RESPONSE
    Respond with data to get and set requests from the manager. (by the agent)
  SET REQUEST
    Initialize and make changes to a value of the network element
  TRAP
    Report an alert or other asynchronous event about a managed subsystem
      In SNMPv1, asynchronous event reports are called traps while they are called notifications in later versions of SNMP.
      In SMIv1 MIB modules, traps are defined using the TRAP-TYPE macro; in SMIv2 MIB modules, traps are defined using the NOTIFICATION-TYPE macro.

## Slide 52: SNMPv2 and structure of management information
Other PDUs were added in SNMPv2, including:
  GETBULK REQUEST
    Faster iterator used to retrieve sequences of management information.
  INFORM
    an acknowledged trap
Typically, SNMP uses UDP ports 161 for the agent and 162 for the manager.
  Manager may send Requests from any available ports (source port) to port 161 in the agent (destination port)
  Agent response will be given back to the source port
  Manager receives traps on port 162
  Agent may generate traps from any available port
Many distributions change these values

## Slide 53: SNMPv2 SMI information modules
The SNMPv2 SMI also specifies information modules
  Specify a group of related definitions
Three types of SMI information modules exist:
  MIB modules
  compliance statements
  capability statements

## Slide 54: SNMPv2 SMI information modules
MIB modules
  Definitions of interrelated managed objects
Compliance statements
  Systematic way to describe a group of managed objects that must be implemented for conformance to a standard
Capability statements
  Indicate the precise level of support that an agent claims with respect to a MIB group
  A NMS can adjust its behavior toward agents according to the capabilities statements associated with each agent.

## Slide 55
SNMPv3

## Slide 56: SNMPv3
SNMPv3 defined by RFC 3411–RFC 3418
  also known as 'STD0062'
SNMPv3 primarily added security and remote configuration enhancements
SNMPv3 is the current standard version of SNMP
  IETF considers earlier versions "Obsolete" or "Historical"

## Slide 57: SNMPv3
SNMPv3 provides important security features:
  Message integrity
    Ensure that a packet has not been tampered with in transit
  Authentication
    Verify that the message is from a valid source
  Encryption of packets
    Prevent snooping by an unauthorized source

## Slide 58: Development and usage

## Slide 59: Version 1
SNMP version 1 (SNMPv1)
  The initial implementation of the SNMP protocol
SNMPv1 operates over protocols such as
  User Datagram Protocol (UDP)
  Internet Protocol (IP)
  OSI Connectionless Network Service (CLNS)
  AppleTalk Datagram-Delivery Protocol (DDP)
  Novell Internet Packet Exchange (IPX)
SNMPv1 is widely used
  The de facto network-management protocol

## Slide 60: Version 1
The first RFCs for SNMP, now known as SNMPv1, appeared in 1988:
  RFC 1065 — Structure and identification of management information for TCP/IP-based internets
  RFC 1066 — Management information base for network management of TCP/IP-based internets
  RFC 1067 — A simple network management protocol
  These protocols were obsoleted by:
  RFC 1155 — Structure and identification of management information for TCP/IP-based internets
  RFC 1156 — Management information base for network management of TCP/IP-based internets
  RFC 1157 — A simple network management protocol

## Slide 61: Version 1
Criticized for its poor security:
  Authentication of clients is performed only by a "community string“
    In effect a type of password, which is transmitted in cleartext
The 80’s design of SNMP V1 was done by a group of collaborators
    Viewed the officially sponsored OSI/IETF/NSF effort (HEMS/CMIS/CMIP) as both
      unimplementable in the computing platforms of the time
      potentially unworkable
SNMP was approved based on a belief that it was an interim protocol needed for taking steps towards large scale deployment of the Internet and its commercialization
In that time period Internet-standard authentication/security was both a dream and discouraged by focused protocol design groups

## Slide 62: Version 2
Version 2 was not widely adopted due to serious disagreements over the security framework in the standard

## Slide 63: Version 2
SNMPv2 (RFC 1441–RFC 1452)
  Revised version 1
  Improvements in the areas of
    Performance, security, confidentiality, and manager-to-manager communications.
  Introduced GETBULK
    Alternative to iterative GETNEXTs
      Retrieving large amounts of management data in a single request
  The new party-based security system in SNMP v2 was not widely accepted
    viewed by many as overly complex

## Slide 64: Version 2
Community-Based Simple Network Management Protocol version 2, or SNMPv2c
  Defined in RFC 1901–RFC 1908
  In its initial stages, this was also informally known as SNMP v1.5.
SNMP v2c comprises SNMP v2
  without the controversial new SNMP v2 security model
  using instead the simple community-based security scheme of SNMP v1
While officially only a "Draft Standard", this is widely considered the de facto SNMP v2 standard.

## Slide 65: Version 2
User-Based Simple Network Management Protocol version 2, or SNMP v2u
  Defined in RFC 1909–RFC 1910
  Compromise:
    Attempted to offer greater security than SNMP v1
    Without incurring the high complexity of SNMP v2
  A variant was commercialized as SNMP v2*
    Mechanism was eventually adopted as one of two security frameworks in SNMP v3

## Slide 66: SNMPv1 & SNMPv2c interoperability
As presently specified, SNMPv2 is incompatible with SNMPv1 in two key areas:
  message formats
  protocol operations.
SNMPv2c messages use different header and protocol data unit (PDU) formats than SNMPv1 messages.
  SNMPv2c also uses two protocol operations that are not specified in SNMPv1.
  Furthermore, RFC 1908 defines two possible SNMPv1/v2c coexistence strategies:
    Proxy agents
    Bilingual network-management systems

## Slide 67: Proxy agents
A SNMPv2 agent can act as a proxy agent on behalf of SNMPv1 managed devices, as follows:
  A SNMPv2 NMS issues a command intended for a SNMPv1 agent
  The NMS sends the SNMP message to the SNMPv2 proxy agent
  The proxy agent forwards Get, GetNext, and Set messages to the SNMPv1 agent unchanged
  GetBulk messages are converted by the proxy agent to GetNext messages and then are forwarded to the SNMPv1 agent
The proxy agent maps SNMPv1 trap messages to SNMPv2 trap messages and then forwards them to the NMS

## Slide 68: Bilingual network-management system
Bilingual SNMPv2 network-management systems support both SNMPv1 and SNMPv2
To support this dual-management environment
  Management application in the bilingual NMS must contact an agent
  NMS then examines information stored in a local database to determine whether the agent supports SNMPv1 or SNMPv2.
Based on the information in the database
  NMS communicates with the agent using the appropriate version of SNMP

## Slide 69: Version 3
Simple Network Management Protocol version 3
  Defined by RFC 3411–RFC 3418
    also known as STD0062
  The IETF recognized as the current standard version of SNMP as of 2004
  The IETF considers earlier versions as "Obsolete" or "Historical"
SNMP implementations often support multiple versions: typically SNMPv1, SNMPv2c, and SNMPv3
  See RFC 3584 "Coexistence between Version 1, Version 2, and Version 3 of the Internet-standard Network Management Framework"

## Slide 70: Resume 11/10

## Slide 71: Version 3
SNMPv3 provides three important services:
  Authentication
  Privacy
  Access control

## Slide 72: Usage examples

## Slide 73: Usage examples
Monitoring device uptimes
  (sysUpTimeInstance)
Inventory of OS versions
  (sysDescr)
Collect interface information
  (ifName, ifDescr, ifSpeed, ifType, ifPhysAddr)
Measuring network interface throughput
  (ifInOctets, ifOutOctets)
Querying a remote ARP cache
  (ipNetToMedia)

## Slide 74: Other SNMP topics

## Slide 75: Autodiscovery
SNMP by itself is simply a protocol for collecting and organizing information
Most toolsets implementing SNMP offer some form of discovery mechanism
  Standardized collection of data common to most platforms and devices
  Used to get a new user or implementer started
One of these features is often a form of automatic discovery
  New devices discovered in the network are polled automatically

## Slide 76: Autodiscovery
For SNMPv1 and SNMPv2c
  Presents a security risk
  Your SNMP read communities will be broadcast in cleartext to the target device
While security requirements and risk profiles vary from organization to organization
  Care should be taken when using a features like these
  Special regard to common environments such as
    Mixed-tenant datacenters
    Server hosting and colocation facilities
    Similar environments

## Slide 77: Negative impact
SNMP implementations vary across platform vendors
  SNMP is often an added feature
    Not an element of the core design
  SNMP's tree structure and linear indexing may not always mate well with the internal data structures that are elements of a platform's basic design
  Using SNMP to query certain data sets may result in high CPU utilization
    Negative effects on operation
    One example of this would be large routing tables
      such as BGP or IGP

## Slide 78: Index shifting
Modular devices may renumber their indexes
  Whenever slotted hardware is added or removed
Index values are typically assigned at boot time
  Remain fixed until the next reboot
Hardware added while the device is 'live' may have their indexes assigned at the end of the existing range
  Reassigned at the next reboot
  Causing a massive shift for all hardware objects that are polled *after* the new addition
Network inventory and monitoring tools may then experience corruption and mismatch polled data
  If unable to account for this behavior

## Slide 79: Security implications
SNMP versions 1 and 2c are subject to packet sniffing
  The clear text community string from the network traffic
  No encryption
All versions of SNMP are subject to bruteforce and dictionary attacks for guessing the community strings/authentication strings,
  Do not implement a challenge-response handshake
SNMP can work over TCP and other protocols
  Most commonly used over UDP
    Connectionless and vulnerable to IP spoofing attacks
  All versions are subject to bypassing device access lists that might have been implemented to restrict SNMP access
    SNMPv3's other security mechanisms should prevent a successful attack

## Slide 80: Security implications
SNMP's configuration (write) capabilities can be misconfigured and used to cause much damage
  'write' capabilities are very rarely used in practice, due to lack of security in SNMP versions before SNMPv3.
  Lack of security is particularly serious with SNMPv1 or v2c over UDP - clear text community strings can be intercepted and combined with IP spoofing
SNMP tops the list of the SANS Institute's Common Default Configuration Issues
  The issue of default SNMP community strings set to ‘public’ and ‘private’
  Number ten on the SANS The Top 10 Most Critical Internet Security Threats for the year 2000
For more detail on SNMP security implications see the CERT SNMP Vulnerabilities FAQ

## Slide 84: RFCs
Base
  RFC 1155: Structure and Identification of Management Information for the TCP/IP-based Internets
  RFC 1156: Management Information Base for Network Management of TCP/IP-based internets
  RFC 1157: A Simple Network Management Protocol (SNMP)
  RFC 1441: Introduction to version 2 of the Internet-standard Network Management Framework
  RFC 1213: Management Information Base for Network Management of TCP/IP-based internets: MIB-II
  RFC 3410 (Informational): Introduction and Applicability Statements for Internet Standard Management Framework
Standard 62
  RFC 3411: An Architecture for Describing Simple Network Management Protocol (SNMP) Management Frameworks
  RFC 3412: Message Processing and Dispatching for the Simple Network Management Protocol (SNMP)
  RFC 3413: Simple Network Management Protocol (SNMP) Application
  RFC 3414: User-based Security Model (USM) for version 3 of the Simple Network Management Protocol (SNMPv3)
  RFC 3415: View-based Access Control Model (VACM) for the Simple Network Management Protocol (SNMP)
  RFC 3416: Version 2 of the Protocol Operations for the Simple Network Management Protocol (SNMP)
  RFC 3417: Transport Mappings for the Simple Network Management Protocol (SNMP)
  RFC 3418: Management Information Base (MIB) for the Simple Network Management Protocol (SNMP)
Best Current Practice
  RFC 3584: Coexistence between Version 1, Version 2, and Version 3 of the Internet-standard Network Management Framework
Proposed
  RFC 3826: The Advanced Encryption Standard (AES) Cipher Algorithm in the SNMP User-based Security Model

## Slide 85: Implementations
Net-SNMP (Net-SNMP: Open source SNMP implementation)
Netsnmpj: Open source SNMP for Java
OpenSNMP: multi-threaded SNMPv3 engine
PySNMP: pure-Python module, BSD license
TinySNMP: an easy to configure minimal SNMPv1 agent
.SNMPv3 for .NET
iReasoning MIB Browser / SNMP Manager (Free)
Net::SNMP : a pure Perl module that implements SNMPv1, v2 and v3 on IPv4 and IPv6
SNMP4J - Free SNMP API for Java Managers and Agents
versatile-serializing.net, .NET library, contains a SNMP V2C implementation

## Slide 86: Post-Quiz: SNMP can
Monitor devices
Change devices
Warn of errors
All of the above
None of the above

## Slide 87: Summary
SNMP is a protocol to define a framework for network management tasks
By itself is just a definition
  Must be “made real” by products