## Slide 1: ITIS 3110 Lab 1
VM Creation & Pi Baking

## Slide 2: Group Project Upcoming
4 members per group
  3 or 5 will be allowed, but verify with instructor first
Start thinking about forming groups now
  Make sure you all have common available times
  Start brainstorming topics later

## Slide 3: General Lab Notes

## Slide 4: Basic Lab Information
Work hard/smart in the labs
  Labs are designed for advanced students
  You will have to lookup information
  You will need to investigate
  You may have to redo steps
  Shut VMs down properly!
  Eject USB devices before disconnecting!
  Backup Work

## Slide 5: Getting Help
Manual pages
  Most commands have a manual page available
  You can access a man page using the ‘man’ command
  Forward slash (/) will search through a man page for a term
  Some configuration files also have man pages
Aren’t certain of a command?
  Use ‘apropos’
  Apropos searches for a keyword in the name and descriptions of all man pages

## Slide 6: Getting Help
Did a command complete successfully?
  Some commands:
    Print no output when they succeed or
    - or -
    Print no output when they fail
  You can check the return value of a command
  A 0 return value means that the command returned successfully
  Run echo $? immediately after a command to check the exit value

## Slide 7: Getting Help
Search the Web
Wikipedia is a fairly good resource for UNIX
Take everything you see with a grain of salt
Pay attention to dates

## Slide 8: Getting Help
Ask for help
  I will try to make a forum available in Canvas for questions
    Upon request of students
  You can always email me or the TAs
  TAs will have office hours in the lab
  Other classmates, but make sure you do your own work

## Slide 9: Text Editors
vi vs. emacs:
  There is an eternal flame war between using vi and emacs
  emacs is often used by programmers
  vi is often used by administrators
    vi has excellent syntax highlighting
  In reality, people stick with the one the know
The vi editor is recommended for the brave and ambitious
  Especially if you anticipate a career as a SysAdmin

## Slide 10: Text Editors
Alternatives:
  nano
    nano is fairly simple
    Always start it as ‘nano –w’
      Otherwise it might fold lines at 80 characters
  pico
  Any editor you feel comfortable with that works with your environment

## Slide 11: Important Note
All submitted labs must have a 302 Lab Exit Activity report attached at the end
  Some printed forms will be in the lab
  Form available online on the labs page

## Slide 12: Labs and Schedule
Labs
  ..\3110Labs.htm
Schedule
  ..\3110LabSchedule.htm

## Slide 13: Lab 1
Creating VMs and Pi image

## Slide 14: Lab Machines
2 Virtual Machines
  1 Server
    Debian
      Very important: NO GUI
  1 Client
    CentOS with GUI
  *** Note the size & start time difference
1 Physical Machine
  Client/Server
    Raspberry Pi Model B
      Version 3 preferred
      All will work but will be slower
      Do not have the GUI auto-start

## Slide 15: Lab Machines
IP addresses
  Each student will have their own subnet
  See Moodle/Posting for list of student subnets
    Make sure your Debian is 172.16.x.10
      * This is needed for DNS to work properly
  If subnets have not yet been assigned use your workstation number as the 3rd octet for the time being

## Slide 16: VM Quirks
Make sure you ALWAYS shut the VMs down properly
  i.e. with shutdown commands
Run VMs off the scratch area on the HD
  Save to flash and/or network storage
The CentOS install has default repositories on the Internet
  Use instructions on Moodle to use internal rpm repository

## Slide 17: General lab tips
Editing files
  When the lab instructions say edit a file:
    Use your favorite editor (nano, vi, emacs, etc.)
    Always make a backup of the file before editing
      Especially before editing the first time!!!!
    Use comments to make restoration of options easy
      Copy the original line and comment
      Make changes to the other

## Slide 18: General lab tips
View/monitor files
  When the lab instructs you to view/monitor
    Use "more", "less“, "cat" or similar tool to view
      cat /var/log/syslog
      cat /var/log/syslog | more
      cat /var/log/messages | less
      less /var/log/syslog
    Use “tail", "less +F " or similar tool to monitor changes
  Never use an editor to monitor a file
    Why?

## Slide 19: Less tips
One of the recommended programs for viewing/monitoring system logs
  Command: less /var/log/syslog
  Inside the less program:
    <Shift-g>
      move to end of file
    <g>
      move to start of file
    <Shift-f>
      enters the monitor mode
      shows you the file updates in real time
      <Ctrl-c> will exit the monitor mode in less
    Use <q> to exit less

## Slide 20: Alternatives
tail filename
  Shows last 10 entries in a file
tail –n 20 filename
  Show last 20 entries
tail –f filename
  Update last entries every few seconds
head
  shows the start of a file
  options same as for tail

## Slide 21: Raspberry Pi
Card sized, single-board computer
  CPU
    ARM 700MHz Processor
  Memory
    512MB (Model B)
  SD Slot (Model B)
    Functions as a hard drive
    Micro SD on the Model B+
  USB Hub
    2 ports (Model B)
    4 ports (Model B+)
  Video
    HDMI
    Composite (Model B only)

## Slide 22: Raspberry Pi
Trivial to change OS
  Swap SD card for a new one!
Many Linuxes ported to ARM
  Raspbian (Debian)
  Pidora (Fedora)
  Arch Linux
  RISC OS
    Not Linux
NooBS (New out of Box Software)
  Six OS in one package
  Can install one at a time
    Changing OS destroys previous OS
  NOT advised for labs!!!!

## Slide 23: Raspberry Pi
Inexpensive
  Model A - $25
    …
  Model B - $35
  Model B+ - $35
  Pi 2 Model B - $35
  Pi 3 Model B - $35
    Includes WiFi !
Required accessories
  Power Supply
    1000ma 5V microUSB
  SD card
    4-8GB (Rasbpian)
    16 GB (Kali) - later
  Optional Accessories
    Keyboard, Mouse
    Monitor
    Hdmi-dvi cable
    Hub
    Case (highly recommended)

## Slide 24: Raspberry Pi
My impressions:
  Base system fast enough for simple server
    Web pages
    XBMC
  Easy to setup and configure
    Full blown Linux
  GUI is a little slow
    Compared to an Intel i7 or AMD Bulldozer
  Great learning tool!

## Slide 25: Raspberry Pi
Extras to consider for home use:
  Powered USB Hub
  Extra SD cards
    4GB minimum
      8 or 16 gives more flexibility and storage
  USB drive for inexpensive "mass storage"
  USB-SD card adapter
    Create your own SD images

## Slide 26: Raspberry Pi
Option:
  Create your Pi image at Home
    Download latest Raspbian
    https://www.raspberrypi.org/downloads/
    Avoid NooBs
  Advantage
    Will have access to latest repository at home
    Can update at home
    Will have latest version
  Disadvantage
    Cannot update in Lab
    May be small differences in Lab vs. Home version

## Slide 27: Get Started