## Slide 1: ITIS 3110 Network Auditing

## Slide 2: overview
networking refresh
protocols refresh

## Slide 3: hubs
Hubs are "dumb" devices that simply act as a repeater
Retransmit incoming packets to all attached devices
  May amplify or recondition
Hubs essentially provide a shared medium
  All devices see all packets

## Slide 4: hubs
Attached devices must implement CSMA/CA
  Carrier Sense Multiple Access with Collision Avoidance
Collisions will occur
  When they do:
    all devices stop transmitting
    perform a random backoff

## Slide 5: hubs
Hubs are rarely seen today
Still necessary to know how they work
  Wireless networks use same principles

## Slide 6: Historical Note
10BASE2
  Coaxial Cable
  BNC T-Connectors
  Terminators
  Thinnet “bus”
    RG58 cable with BNC Connectors
  Worked in “half-duplex”
    E.g. could only send or receive at one time

## Slide 7: switches
Switches typically use a CAM table
  Maps MAC addresses of attached devices into physical ports on the switch
CAM = Content Addressable Memory
  ≈ associative array

## Slide 8: switches
MAC to port mapping
  Allows the switch to only transmit a packet the destination port
Mapping speeds up throughput
  Collisions no longer possible
  Able to run in full-duplex
    Dedicated transmit and receive lines

## Slide 9: mac address
MAC - Media Access Control
  Unique 48-bit number assigned to a network card
  6 octets
  Now formally known as EUI-48
First three octets of MAC address indicate the manufacturer
  IEEE OUI Database
Packets are sent to MAC addresses
  e.g. Ethernet frames
EUI-64 also defined
  Used by IPv6, ZigBee, FireWire

## Slide 10: mac addresses
MAC addresses only used on the local network
  Local NIC to local NIC
If IP address is outside local network
  Ethernet frame is sent to MAC address of the gateway or router
Gateway sends frame to MAC address of its gateway

## Slide 11: gateways
Gateway is specific term for a type of router
  A router attached to an edge network
    e.g. your local network
Static routes can map IP blocks to certain gateways
Default route is the gateway that should be used if no other route matches the destination

## Slide 12: “Interesting” Protocols
Transport Layer:
  TCP
    Transmission Control Protocol
  UDP
    User Datagram Protocol
“Network Layer”:
  ICMP
    Internet Control Message Protocol
Other, special-purpose protocols exist

## Slide 13: icmp
Internet Control Message Protocol
Does not carry "data"
  Relays network status
Used for:
  Error notification
  Host availability (ping)
  Network congestion notification
http://en.wikipedia.org/wiki/Internet_Control_Message_Protocol

## Slide 14: typical icmp control messages
type | description
0 | echo reply
3 | destination unreachable
8 | echo request
11 | time exceeded

## Slide 15: destination unreachable (3)
Generated when a packet was not delivered successfully
16 codes for different failure modes
  e.g.
    0: Destination network unreachable
    1: Destination host unreachable
    2: Destination protocol unreachable
    3: Destination port unreachable
    …
    6: Destination network unknown
    7: Destination port unknown
    …
    13: Communication administratively prohibited
    …

## Slide 16: time exceeded (11)
TTL
  Time to live
Every packet has a TTL associated with it
  TTL is decremented by every router it goes through
  A router will discard a packet and generate a ‘time exceeded’ message if the packet’s TTL has reached zero
https://subinsb.com/default-device-ttl-values

## Slide 17: ping (8) and (0)
Uses ‘echo request (8)’ and ‘echo reply (0)’
  Determines if a remote host is "alive"
    .e.g. responding
$ ping -c4 www.google.com
PING www.l.google.com (74.125.47.105): 56 data bytes
64 bytes from 74.125.47.105: icmp_seq=0 ttl=54 time=21.768 ms
64 bytes from 74.125.47.105: icmp_seq=1 ttl=54 time=20.363 ms
64 bytes from 74.125.47.105: icmp_seq=2 ttl=54 time=19.071 ms
64 bytes from 74.125.47.105: icmp_seq=3 ttl=54 time=22.606 ms
--- www.l.google.com ping statistics ---
4 packets transmitted, 4 packets received, 0.0% packet loss
round-trip min/avg/max/stddev = 19.071/20.952/22.606/1.350 ms

## Slide 18: traceroute
Determines the route packets take to the destination
Repeatedly sends packets
  With TTLs starting with 1 incrementing to n
    waits for ‘time exceeded’ messages
      from each router on the path to the destination
Packets sent can be ICMP, TCP, UDP, or GRE
  UNIX use UDP by default
  Windows uses ICMP by default

## Slide 19: traceroute
Note that this traceroute did not finish
  UNCC blocks UDP and ICMP at their gateway
$ traceroute uncc.edu
traceroute to uncc.edu (152.15.216.33), 64 hops max, 52 byte packets
1 192.168.1.1 (192.168.1.1) 1.056 ms 0.654 ms 0.587 ms
2 10.110.192.1 (10.110.192.1) 8.880 ms 9.750 ms 8.941 ms
3 24.93.75.204 (24.93.75.204) 11.861 ms 11.419 ms 14.005 ms
4 ge-2-2-0.rlghncrdc-pop1.southeast.rr.com (24.93.64.171) 16.757 ms 16.511 ms 50.779 ms
5 ae14.chrlncpop-rtr1.southeast.rr.com (24.93.64.25) 17.390 ms 16.849 ms 17.834 ms
6 ten1-3.chrlncsa-p-rtr01.southeast.rr.com (24.93.73.57) 18.991 ms 17.712 ms 16.274 ms
7 ten3-0-0.gnboncsg-pe-rtr01.southeast.rr.com (24.93.73.34) 21.275 ms 21.035 ms 21.411 ms
8 ten3-0-0.gnboncsg-p-rtr01.southeast.rr.com (24.93.73.73) 32.690 ms 22.018 ms 22.016 ms
9 ten3-0-0.rlghncrdc-pe-rtr01.southeast.rr.com (24.93.73.38) 22.741 ms 21.008 ms 22.053 ms
10 por100.twcc.rlghnc-a-c2702.nc.rr.com (24.27.255.255) 22.474 ms 21.831 ms 22.125 ms
11 rrcs-96-10-0-254.se.biz.rr.com (96.10.0.254) 23.035 ms 21.208 ms 25.354 ms
12 chltcrs-gw-to-rtpcrs-gw.ncren.net (128.109.212.2) 41.055 ms 37.017 ms 26.282 ms
13 chlt7600-gw-sec-to-chltcrs-gw.ncren.net (128.109.9.14) 25.470 ms 25.728 ms 26.732 ms
14 uncc-gw-gige-to-chlt7600-gw.ncren.net (128.109.246.30) 40.711 ms 27.710 ms 27.681 ms
15 * * *
16 * * *
17 * * *
18 * * *

## Slide 20: traceroute
This traceroute reached its destination
$ traceroute -P icmp google.com
traceroute: Warning: google.com has multiple addresses; using 74.125.45.103
traceroute to google.com (74.125.45.103), 64 hops max, 72 byte packets 1 192.168.1.1 (192.168.1.1)
1.196 ms 0.578 ms 0.541 ms
2 10.110.192.1 (10.110.192.1) 7.865 ms 9.276 ms 7.655 ms
3 24.93.75.204 (24.93.75.204) 10.706 ms 10.860 ms 22.169 ms
4 xe-7-0-3.rlghncpop-rtr1.southeast.rr.com (24.93.64.21) 18.732 ms 18.102 ms 15.791 ms
5 ae-3-0.cr0.dca10.tbone.rr.com (66.109.6.80) 23.111 ms 24.145 ms 26.099 ms
6 ae-2-0.pr0.dca10.tbone.rr.com (66.109.6.169) 21.863 ms 27.766 ms 23.933 ms
7 74.125.49.181 (74.125.49.181) 24.201 ms 22.925 ms 24.358 ms
8 216.239.48.108 (216.239.48.108) 25.038 ms 26.261 ms 23.763 ms
9 66.249.95.149 (66.249.95.149) 28.755 ms 29.010 ms 27.522 ms
10 72.14.232.213 (72.14.232.213) 30.101 ms 29.036 ms 28.282 ms
11 209.85.253.133 (209.85.253.133) 28.409 ms 209.85.253.145 (209.85.253.145) 36.219 ms 28.585 ms
12 yx-in-f103.1e100.net (74.125.45.103) 31.907 ms 28.767 ms 29.679 ms

## Slide 21: tcp
Transmission Control Protocol
Stateful protocol
  Connections (Sessions) must be established before use
Guarantees delivery
Can detect and compensate for out-of-order delivery

## Slide 22: select tcp flags
ACK
  Acknowledgement
    All client packets must set after the initial SYN
FIN
  Closing connection
    No further data will be sent from sender
RST
  Reset connection
SYN
  Start of connection
    Initial packet from client will set SYN

## Slide 23: tcp 3-way handshake

## Slide 24: closing tcp connection

## Slide 25: tcp resets
Signals something is wrong with the connection
  It must be re-established
Sent when an endpoint is confused
  e.g. received data for a closed connection
Can be sent by a network device between endpoints
  e.g. NAT device when the connection expires from its internal table

## Slide 26: udp
User Datagram Protocol
  Stateless protocol
Packets may be lost or arrive out-order
Often used where speed is required
  Lost packets are acceptable
  Sending/receiving program may do "something"
Many services built on UDP implement their own state tracking

## Slide 27: arp
Address Resolution Protocol
Runs directly on top of ethernet
  Same level as IPv4 or IPv6
Maps IPv4 addresses to MAC addresses
  IPv6 uses Neighbor Discovery Protocol instead of ARP
Can run on protocols other than ethernet
Can map addresses other than IPv4

## Slide 28: arp packets
Request
  Search for MAC address corresponding to an IP address
Reply
  Response from MAC address telling requesting host that it has the specified IP address
Probe
  Special type of request packet
Announcement
  Special type of probe packet

## Slide 29: arp request
Field | Contents
Source IP | requesting IP
Source MAC | requesting MAC
Target IP | destination IP
Target MAC | broadcast

## Slide 30: arp reply
Field | Contents
Source IP | answering IP
Source MAC | answering MAC
Target IP | requesting IP
Target MAC | requesting MAC

## Slide 31: arp probe
Used to detect IP address conflicts
  Make sure no one has your address
All hosts should generate a probe when connecting to a network
A number of probes are sent with random wait times
If any ARP packets are received with same sender IP address, there is a conflict
  requests or responses

## Slide 32: arp probe
Field | Contents
Source IP | zeros
Source MAC | host mac address
Target IP | requested IP
Target MAC | ignored (zeros)

## Slide 33: arp announce
aka gratuitous ARP
Notifies other hosts that an IP address maps to a MAC address

## Slide 34: arp announce
Field | Contents
Source IP | host IP
Source MAC | host MAC
Target IP | host IP
Target MAC | host MAC

## Slide 35: arp table
All hosts maintain an ARP table containing mappings of IP address to MAC address
  Table is consulted before ARP requests are sent to the network
  Table may be updated to include information from gratuitous ARP announces
    As well as ARP replies to other hosts requests
  Static maps can be added to ARP table

## Slide 36: arp table
$ /sbin/arp -an
? (172.30.1.70) at 00:14:5E:6D:62:98 [ether] on eth0
? (172.30.1.1) at 00:14:5E:6D:82:20 [ether] on eth0
? (172.30.1.6) at 00:14:5E:6D:92:14 [ether] on eth0
? (172.30.1.8) at 00:14:5E:6D:90:C6 [ether] on eth0
? (172.30.1.99) at 00:1A:64:BD:49:56 [ether] on eth0
? (172.30.1.11) at 00:14:5E:6D:8E:8A [ether] on eth0
? (172.30.30.4) at <incomplete> on eth0
? (172.30.2.1) at 00:14:5E:5A:A6:0A [ether] on eth0
? (172.30.100.8) at 00:14:5E:E1:5F:F8 [ether] on eth0
? (172.30.1.52) at 00:14:5E:6D:71:FC [ether] on eth0
? (172.30.1.51) at 00:14:5E:6D:8E:6E [ether] on eth0
? (172.30.30.3) at <incomplete> on eth0
? (172.30.1.66) at 00:14:5E:6D:81:A0 [ether] on eth0
? (204.84.7.1) at 00:07:B4:00:04:01 [ether] on eth1
? (204.84.7.125) at 00:22:90:FF:DC:59 [ether] on eth1

## Slide 37: whois
IP blocks are registered to organizations
Can often map an IP block back to an organization using whois
whois can also be used to map domain names to organizations

## Slide 38: whois
$ whois 152.15.216.33
[Querying whois.arin.net][whois.arin.net]
...
OrgName: University of North Carolina at Charlotte
OrgId: UNCAC
Address: Information Technology Services
Address: 9201 University City Blvd
City: Charlotte
StateProv: NC
PostalCode: 28223-0001
Country: US
RegDate: 1991-06-07
Updated: 2010-01-05
Ref: http://whois.arin.net/rest/org/UNCAC
...

## Slide 39: warning
Commands mentioned past here have consequences
Many of these commands send malformed data to see how systems respond
This can cause stability problems
Attempting any of these on UNCC’s network will get you banned
Packet sniffing on networks you do not own may be illegal

## Slide 40: network scanning
Scanning of network attached hosts to determine:
  Used IP addresses
  Operating Systems
  Available services
  OS and service versions

## Slide 41: network scanning
Has many uses, legitimate and otherwise
  Detecting rogue machines & services
  Auditing visible services
  Verifying firewall rules

## Slide 42: tcp scan types
Many different scan types exist
  Most exploit subtle loopholes in the TCP specification
Connect
Complete 3-way handshake
SYN
  Only SYN flag set
  Starts but does not complete TCP handshake

## Slide 43: tcp scan types
FIN stealth
  Only FIN flag is set
Xmas
  Sets FIN, PSH, URG flags
Null
  Sets no flags

## Slide 44: nmap
Open-source port scanner
Capable of detecting open services (ports) on hosts
Supports TCP, UDP, other protocols
Fast & feature rich

## Slide 45: nmap flags
-sS
  SYN scan
-sT
  Connect scan
-P0
  do not ping hosts first
-A
  OS, version detection, script scanning, and traceroute

## Slide 46: nmap
Typical report:
PORT STATE SERVICE 21/tcp open ftp 22/tcp open ssh 23/tcp open telnet 80/tcp open http 111/tcp open rpcbind 113/tcp open auth 199/tcp open smux 554/tcp open rtsp 873/tcp open rsync 1521/tcp open oracle 2401/tcp open cvspserver 6000/tcp open X11 7070/tcp open realserver 8009/tcp open ajp13 8080/tcp open http-proxy

## Slide 47: nessus
Vulnerability scanner
  Commercial scanner
  Costs $$$
  Limited home version available
Takes port scanning one step further
Able to tell you if services on hosts are vulnerable and to what
Generates nice reports

## Slide 48: packet sniffing
Capturing packet data from a live network
Need to put the interface in promiscuous mode
  To capture data bound for other hosts

## Slide 49: switches
Switches complicate packet sniffing
  They do not retransmit all traffic to every host
There are ways around switches

## Slide 50: mac flooding
Generate thousands of spurious ARP announcements
Overflow the switch’s CAM table
  Forcing it to act like a hub
You can see and sniff all traffic while the switch is rebuilding its CAM table
Modern switches usually have enough memory to make this impractical

## Slide 51: arp spoofing
Generate many ARP announcements per second
Claiming your MAC address has the IP addresses you wish to intercept
If you are not careful you can take out the entire network when ARP spoofing

## Slide 52: man in the middle
Attack where you place yourself between the two endpoints that you wish to intercept traffic from
Allows you to alter data passing between the two endpoints
ARP spoofing is a type of MITM attack

## Slide 53: tcpdump
Gold standard of packet sniffers
Has a simple filter language that allows you to filter traffic
Filter on
  IP
  Protocol
  Port
  etc.

## Slide 54: tcpdump
# tcpdump -i en1
tcpdump: verbose output suppressed, use -v or -vv for full protocol decode
listening on en1, link-type EN10MB (Ethernet), capture size 65535 bytes
02:24:12.342774 IP ch3.sourceforge.net.https > 192.168.1.35.50197: Flags [R.], seq 4086174604, ack 3660086855, win 178, length 002:24:12.342862 IP ch3.sourceforge.net.http > 192.168.1.35.50199: Flags [R.], seq 1190843218, ack 1076026833, win 167, length 002:24:12.342866 IP ch3.sourceforge.net.http > 192.168.1.35.50198: Flags [R.], seq 2231290586, ack 479167141, win 167, length 002:24:12.342867 IP ch3.sourceforge.net.https > 192.168.1.35.50196: Flags [R.], seq 1796962400, ack 4043912392, win 178, length 002:24:12.643627 IP 192.168.1.35.54560 > 192.168.1.1.domain: 41399+ PTR? 35.1.168.192.in-addr.arpa. (43)
02:24:12.647439 IP 192.168.1.1.domain > 192.168.1.35.54560: 41399 NXDomain* 0/0/0 (43)
02:24:12.652922 IP 192.168.1.35.54259 > 192.168.1.1.domain: 42748+ PTR? 60.181.34.216.in-addr.arpa. (44)
02:24:12.726921 IP 192.168.1.1.domain > 192.168.1.35.54259: 42748 1/0/0 PTR ch3.sourceforge.net. (77)
02:24:13.728481 IP 192.168.1.35.62201 > 192.168.1.1.domain: 62577+ PTR? 1.1.168.192.in-addr.arpa. (42)
02:24:13.733818 IP 192.168.1.1.domain > 192.168.1.35.62201: 62577 NXDomain* 0/0/0 (42)

## Slide 55: wireshark
Protocol analyzer
Includes packet sniffing
Can filter captured packets ala tcpdump
Allows deep inspection of packets
Can filter packets using a display filter
Can reconstruct conversations

## Slide 56: tshark
Command line interface to wireshark

## Slide 57: tshark
# tshark -i en1 -R http.request
Capturing on en1
0.047603 192.168.1.35 -> 72.14.209.104 HTTP GET / HTTP/1.1
0.156170 192.168.1.35 -> 72.14.209.104 HTTP GET /intl/en_ALL/images/srpr/logo1w.png HTTP/1.1
0.178360 192.168.1.35 -> 72.14.209.104 HTTP GET /extern_js/f/CgJlbhICdXMrMEU4ACwrMFo4ACwrMA44ACwrMBc4ACwrMCc4ACwrMDw4ACwrMFE4ACwrMFk4/zznblRL6LCM.js HTTP/1.1
0.349597 192.168.1.35 -> 72.14.209.104 HTTP GET /ig/cp/get?hl=en&gl=us HTTP/1.1
0.349964 192.168.1.35 -> 72.14.209.104 HTTP GET /csi?v=3&s=webhp&action=&e=17259,18168,26637,27164,27182,27284&ei=ZlDJTMT5NpKYtgeE04nMDw&expi=17259,18168,26637,27164,27182,27284&imc=1&imn=1&imp=1&rt=prt.71,xjsls.73,ol.188,iml.101,xjses.213,xjsee.237,xjs.243 HTTP/1.1

## Slide 58: ettercap
Network sniffer
Has tool for ARP spoofing built-in
  ARP poisoning
Makes it incredibly easy to detect clear-text passwords going across the network
  Makes MITM easy

## Slide 59: ettercap
Some features:
  ARP poisoning
  Plug-in support
  Character injection
  Password collecting for various programs/protocols
  OS Fingerprinting
  Kill select connections
  Hijack DNS requests
  Passive LAN scanning