## Slide 1: SNMP
http://en.wikipedia.org/wiki/SNMP

## Slide 2: SNMP
Simple Network Management Protocol

## Slide 3: WHAT IS IT?

## Slide 4: SNMP
Simple Network Management Protocol
  Part of the internet protocol suite
    Defined by the Internet Engineering Task Force (IETF)
  Used by network management systems
    Monitor network-attached devices for conditions that warrant administrative attention
    Manage said systems

## Slide 5: SNMP
Consists of a set of standards for network management
  Application Layer protocol
  Database schema
  Set of data objects

## Slide 6: SNMP
SNMP exposes data
  Variables on the managed systems
  Describe the system configuration
Variables can be queried by managing applications
  Sometimes set

## Slide 7: OVERVIEW AND BASIC CONCEPTS

## Slide 8: Overview and basic concepts
Typical SNMP environment:
  Large number of systems to be managed
  One or more systems manage them
An agent :
  Software component
  Runs on each managed system
  Reports information via SNMP to the managing systems

## Slide 9: Overview and basic concepts
SNMP agents reports data of interest on the managed systems
  Variables such as:
    "free memory"
    "system name"
    "number of running processes"
    "default route"
    "number of pages printed"
    etc.

## Slide 10: Overview and basic concepts
Managing systems can retrieve the information through protocol operations
  GET
  GETNEXT
  GETBULK
Agents can send data without being asked using protocol operations
  TRAP
  INFORM

## Slide 11: Overview and basic concepts
Management systems can
  Send configuration updates
  Send controlling requests
Uses the SET protocol operation to actively manage a system

## Slide 12: Overview and basic concepts
Configuration and control operations:
  Only used when changes are needed to the network infrastructure
Monitoring operations:
  Usually performed on a regular basis

## Slide 13: Overview and basic concepts
Variables accessible via SNMP are organized in hierarchies
Management Information Bases (MIBs)
  Contains the hierarchies and other metadata describing each variable’s
    type
    description

## Slide 14: MANAGEMENT INFORMATION BASES
MIBs

## Slide 15: Management Information Bases
SNMP itself does not define which information a managed system should offer
  e.g. variables
SNMP uses an extensible design
  Available information defined by management information bases
    MIBs

## Slide 16: Management Information Bases
MIBs describe the structure of the management data of a device subsystem
  Use a hierarchical namespace containing object identifiers
    OID
  Each OID identifies a variable that can be read or set via SNMP
MIBs use a notation defined by ASN.1

## Slide 17: Management Information Bases
MIB hierarchy can be depicted as:
  A tree with a nameless root
  Levels which are assigned by different organizations
Top-level MIB OIDs belong to different standards organizations
Mid-level object IDs are allocated by associated organizations

## Slide 18: Management Information Bases

## Slide 19: Management Information Bases
Model permits management across all layers of the OSI reference model
  Can extend into applications
    databases
    email
    Java EE reference model
    Etc.
  MIBs can be defined for area-specific information and operations

## Slide 20: Management Information Bases
A managed object1 is one of any number of specific characteristics of a managed device
  Managed objects comprise one or more object instances which are essentially variables
    Identified by their OIDs
  1sometimes called an MIB object, an object, or a MIB

## Slide 21: Management Information Bases
Two types of managed objects exist:
  Scalar objects
    Define a single object instance
  Tabular objects
    Define multiple related object instances
    Grouped in MIB tables

## Slide 22: Management Information Bases
Example of a managed object
  atInput
    a scalar object that contains a single object instance
      An integer value
      Indicates the total number of input AppleTalk packets on a router interface
Object identifier (or object ID or OID)
  Uniquely identifies a managed object in the MIB hierarchy

## Slide 23: SNMP ARCHITECTURE

## Slide 24: SNMP architecture
SNMP framework consists of
  Master agents
  Subagents
  Management stations

## Slide 25: SNMP Agents:
Managed devices can be any type of device including, but not limited to:
  Routers and access servers
  Switches and bridges
  Hubs
  IP telephones
  Computer hosts
  Printers
Key elements:
  Has a CPU
  Has networking

## Slide 26: Master agent
Software running on an SNMP-capable network component
  For example a router
    Responds to SNMP requests from the management station
Acts as a:
  Server in client-server architecture terminology
  Daemon in operating system terminology
Relies on subagents to provide information about the management of specific functionality
Can also be referred to as managed objects

## Slide 27: Subagent
A piece of software running on an SNMP-capable network component
  Implements the information and management functionality defined by a specific MIB of a specific subsystem
    For example the Ethernet link layer

## Slide 28: Subagent
Some capabilities of the subagent are:
  Gathering information from managed objects
  Configuring parameters of the managed objects
  Responding to managers' requests
  Generating alarms or traps

## Slide 29: Management station
Manager or management station
  Final component in the SNMP architecture
Functions as the equivalent of a client in the client-server architecture
  Issues requests for management operations
    On behalf of a administrator or application
  Receives traps from agents

## Slide 30: Odd note for SNMP
Many servers
  Each agent is a server
  Most of the components are managed network devices
Few clients
  Management stations are clients
  Few management station

## Slide 31: Vulnerability Assessment and System Assurance

## Slide 32: SNMP Basics
SNMP – Simple Network Management Protocol (V1/V2/V3)
Uses ASN.1 notation
udp port 161 – SNMP get/sets
udp port 162 – SNMP traps
MIB – Management Information Base (it’s not a database, more of a mapping file)
OID – Object Identifier (Tells where in the Object Tree the value is located, I.E. 1.3.6.1.2.1.1.1 = iso.org.dod.internet.mgmt.mib-2.system.sysDescr))
snmpget – getting the MIB Value
snmpwalk – getting all of the MIB Values from a point in the tree
snmpset – setting a MIB value
snmptrap – Sending an alert to a SNMP trap daemon
SNMP V1 is still the most commonly deployed version

## Slide 33: Enumerating System using SNMP
SNMP is supported on most network devices and servers
    Provides abundant amount of information
Using the free SNMP utilities from http.//net-snmp.sourceforge.net:
C:\snmp\bin> snmpwalk -c public -v1 172.16.1.1 1.3.6.1.2.1.1
SNMPv2-MIB::sysDescr.0 = STRING: Hardware: x86 Family 6 Model 8 Stepping 6 AT/AT COMPATIBLE - Software: Windows 2000 Version 5.0 (Build 2195 Uniprocessor Free)
SNMPv2-MIB::sysObjectID.0 = OID: SNMPv2-SMI::enterprises.311.1.1.3.1.1
SNMPv2-MIB::sysUpTime.0 = Timeticks: (17485) 0:02:54.85
SNMPv2-MIB::sysContact.0 = STRING:
SNMPv2-MIB::sysName.0 = STRING: MYServer
SNMPv2-MIB::sysLocation.0 = STRING:
SNMPv2-MIB::sysServices.0 = INTEGER: 79

## Slide 34: Enumerating System using SNMP
SNMP MIB Lookup: Most vendors make their MIB available to their customers
http://tools.cisco.com/Support/SNMP/do/BrowseOID.do? local=en&substep=2&translate=Translate&tree=NO
proprietary MIBs are located under:
1.3.6.1.4.1 – iso.org.dod.internet.private.enterprise.
Example of Interesting MIB:
1.3.6.1.4.1.522.3.4.1-iso(1).org(3).dod(6).internet(1).private(4).enterprises(1).aironet(522).awcVx(3).awcFtp(4)
See next pages

## Slide 35
awcFtp | 1.3.6.1.4.1.522.3.4
defaultFileServer | 1.3.6.1.4.1.522.3.4.1
awcFileXferFileFirmwareRadio0 | 1.3.6.1.4.1.522.3.4.10
awcFileXferFileWebUI | 1.3.6.1.4.1.522.3.4.11
awcFileXferFileFpgaPcmcia | 1.3.6.1.4.1.522.3.4.12
awcFileXferTftpPort | 1.3.6.1.4.1.522.3.4.13
awcFileXferFtpDirectory | 1.3.6.1.4.1.522.3.4.14
awcFileXferFilesFLASH | 1.3.6.1.4.1.522.3.4.17
awcFileXferFileFirmwareRadio1 | 1.3.6.1.4.1.522.3.4.18
awcFileXferProtocol | 1.3.6.1.4.1.522.3.4.2
awcFileXferUser | 1.3.6.1.4.1.522.3.4.3
awcFileXferPassword | 1.3.6.1.4.1.522.3.4.4
awcFileXferCmdInvokeFileLoad | 1.3.6.1.4.1.522.3.4.5
awcFileXferCmdStatusFileLoad | 1.3.6.1.4.1.522.3.4.6
awcFileXferCmdInvokeFileSave | 1.3.6.1.4.1.522.3.4.7
awcFileXferCmdStatusFileSave | 1.3.6.1.4.1.522.3.4.8
awcFileXferFileFirmwareSystem | 1.3.6.1.4.1.522.3.4.9

## Slide 36: Information Gathering using SNMP
- -- awcFtp (4)
| |
| | -- defaultFileServer (1) object Details
| |
| | -- awcFileXferProtocol (2)
| |
| | -- awcFileXferUser (3)
| |
| | -- awcFileXferPassword (4)
| |
| | -- awcFileXferCmdInvokeFileLoad (5)
| |
| | -- awcFileXferCmdStatusFileLoad (6)
| |
| | -- awcFileXferCmdInvokeFileSave (7)
| |
| | -- awcFileXferCmdStatusFileSave (8)
| |
| | -- ...

## Slide 37: Examining the MIB
1.3.6.1.4.1.522.3.7.1.1 – Aironet Wireless Access Point User Manager
- -- awcUserMgr (7)
|
- -- userMgrConfigTable (1)
| |
| - -- userMgrConfigEntry (1) object Details
| |
| | -- userMgrUserIndex (1)
| |
| | -- userMgrUserName (2)
| |
| | -- userMgrPassword (3)
| |
| | -- userMgrCapabilities (4)
| |
| | -- userMgrStatus (5)
Looking at the description of the MIB:
userMgrPassword OBJECT-TYPE SYNTAX OCTET STRING(SIZE(0..24)) ACCESS read-write
STATUS mandatory DESCRIPTION "The SHA-1 hashed password of the user in the user manager.
When a plaintext password is written, it is automatically replaced by the SHA-1 Secure Hash of that
plaintext, prefixed by a 4-octet magic cookie. Max. string length is 24 octets." ::= {
userMgrConfigEntry 3 }

## Slide 38: SNMP Vulnerabilities
default SNMP write community string ‘private’
default SNMP read community string ‘public’
SNMP community string can be captured using a sniffer
For example, to set the user manager password for a Cisco Aironet Wireless Access Point running vXworks firmware:
snmpset –c private –v1 ip_address 1.3.6.1.4.1.522.3.7.1.1 OctetString “value of the SHA1 hash”

## Slide 39: SNMP Vulnetabilities
Careful what you put in
Some MIB can have “sensitive” data
  E.g. location of a server or router
    Country
    City
    Building number
    Floor
    Room

## Slide 40: SNMP Countermeasures
Use SNMP V3 which has better security model
  user level security
  SNMP V1 only has read or write access
Using Access Control Lists (ACL) to allow only specific IP or ranges SNMP access to network infrastructure devices (router, switches)
Use uncommon SNMP community strings
Disable SNMP on non-network infrastructure devices
  For windows devices, use WMI instead (Windows Management Instrumentation)