## Slide 1: Wireless I

## Slide 2: Haktip-9
Six Modes of Wireless

## Slide 3: Six Modes of Wireless – Notes
Master
  Access Point or base station
Managed
  Aka Infrastructure Mode
  Access point or base station
  Clients or stations
Ad-hoc
  Peer-to-peer
    Informal network
Mesh
  “planned” ad-hoc
  Self healing if a node goes down
Repeater
  Connects and repeats
  Extends range of a network
Monitor
  Monitor all traffic

## Slide 4: Six Modes of Wireless - Questions
What is Ad Hoc Mode?
  Peer to peer connection
  All need the same essid
What mode would you use to extend the cover of your wifi:
  Repeater

## Slide 5: Haktip-11
802.11 Protocols

## Slide 6: 802.11 Protocols – Notes
WiFi: trademark
ISM: Industrial, Scientific, Medical
Protocol Letters
  802.11a
    54Mbs
    5GHz band
    “Enterprise”
  802.11b
    11Mbs
      ~6-7 MBS
    2.4GHz band
    csma/ca
  802.11g
    54Mbs
    2.4GHz band
    Backwards compatible with 802.11b

## Slide 7: 802.11 Protocols – Questions
What protocol is backwards compatible with 802.11b
  802.11g
  What happens if a b is on a g
    Run at b speed (11meg)
What does ISM stand for
  Industrial, Scientific, Medical
  BW:
    900MHz
    2.4GHz
    5.0GHz

## Slide 8: Haktip-13
Channels and Interference

## Slide 9: Channels and Interference – Notes
2.4GHz band
  14 channels
    Channels 1, 6, 11, and 14 are “clear”
      Don’t overlap any other channel
    1-11 North America
    1-13 “world”
    +14 Japan
  22 MHZ channel width
  5 MHz channel separation
5.0 GHz band
  Has other channels
FCC Part 15
  ISM – play nice together

## Slide 10: Channels and Interference – Questions
In Wifi what is a channel
  A band of spectrum
  A range of freq. carrying information
In the 2.4GHz range what is the channel bandwidth
  22MHz
  What is the separation on 1-13
    5MHz

## Slide 11: Haktip-15
802.11n

## Slide 12: 802.11n – Notes
MIMO
  Multiple Input Multiple Output
2.4GHz and 5.0GHz bands
Backwards compatible with previous standards
20 and 40 MHz channel width
Twice the range
600Mb max band width
  4 simultaneous data streams
  Date rate: 7.2 to 150 Mbps per channel
802.11ac being developed
  8 MIMO streams
  80 and 160 MHz bandwidth for the channels
  Max 6.93 Gbps

## Slide 13: 802.11n – Questions
Max speed for 802.11n
  600Mbps
What does MIMO stand for
  Multiple Input / Multiple Output
  What doest that meant
    Multi channel at the same time