## Slide 1: Wireless Modes

## Slide 2: Wireless Modes
AP mode
Client mode
Client Bridged mode
Repeater
Repeater bridge
Ad-Hoc mode

## Slide 3: Wireless Modes
AP mode
  The default
  Most common mode for all wireless routers
    Also called Infrastructure mode.
  Router acts as an central connection point to which wireless clients can connect

## Slide 4: Wireless Modes
Client mode
  Radio interface is used to connect the internet-facing side of the router (i.e., the WAN) as a client to a remote access point
  NAT or routing are performed between WAN and LAN, like in "normal" gateway or router mode
  Use this mode, e.g., if your internet connection is provided by a remote access point, and you want to connect a subnet of your own to it

## Slide 5: Wireless Modes
Client Bridged mode
  The radio interface is used to connect the LAN side of the router to a remote access point
  The LAN and the remote AP will be in the same subnet
    Called a "bridge" between two network segments
  WAN side of the router is unused
    Can be disabled.
  Use this mode, e.g., to make the router act as a "WLAN adapter" for a device connected to one of its LAN Ethernet ports

## Slide 6: Wireless Modes
Repeater
  A repeater simply regenerates a network signal in order to extend the range of the existing network infrastructure
  A WLAN repeater does not physically connect by wire to any part of the network
    Instead, it receives radio signals (802.11 frames) from an access point, end user device, or another repeater and retransmits the frames
  Makes it possible for a repeater located in between an access point and distant user to act as a relay for frames traveling back and forth between the user and the access point

## Slide 7: Wireless Modes
Repeater bridge
  A wireless bridge connects two LAN segments with a wireless link
  The two segments are in the same subnet and look like two Ethernet switches connected by a cable to all computers on the subnet
  Since the computers are on the same subnet, broadcasts reach all machines
  DHCP clients in one segment can get their addresses from a DHCP server in the other segment

## Slide 8: Wireless Modes
Ad-Hoc mode
  Peer to peer wireless connections
  Clients running in Ad-Hoc mode can connect to each other as required without involving central access points