## Slide 1: Testing Printers (and Other Devices)
Chapter 8

## Slide 2: Overview
This chapter will concentrate on testing printers, but the concepts can be extended to testing any peripheral

## Slide 3: Some General Issues in Configuration Testing
Hardware configuration concerns
  What printers may be used
  What video cards, monitors and modes are supported
  Which brands and what type of mice (serial, ps/2, usb)
  What configuration of memory is required/supported
  What types and models of computer are supported
  What operating systems and versions are supported

## Slide 4: Some General Issues in Configuration Testing
Video card example
  Many standards
    Old
      CGA, EGA, HMGA, MCGA, MDA
    Current
      Standard aspect (4:3)
        VGA, SVGA, XGA, SXGA, UXGA, etc…
      Wide formats (16:9 and 16:10)
        WHXGA and many more!
  What standard(s) must you support
    What brand and model
      nVidia
      ATI
      Intel
      Other?
    What API Standards
      DirectX
      OpenGL

## Slide 5: Some General Issues in Configuration Testing
Considerations
  Cannot test all possible hardware combinations
  Understand supported hardware thoroughly
    Use understanding to classify equivalent machines
    Use independent resources
      Don’t trust manufacturers specs
    Understand “perfect” resolution vs. “just like”

## Slide 6: Some General Issues in Configuration Testing
Considerations
  Analyze the market
    What devices do the customers use or want to use
  Analyze the device
    How does the device work
    How will it impact testing
  Analyze the way the software uses the device
    Can devices be grouped
      Same errors
      Similar functions

## Slide 7: Some General Issues in Configuration Testing
Considerations
  Save time
    Test only one device per group
      Get rid of gross errors
  Improve efficiency
    Automate tasks when possible
    Use precise planning and recordkeeping
  Share your experience
    Organize and share results so next and other project can learn
  Does this type of device interact with other devices
    Pick some other devices and do a quick check with the primary device

## Slide 8: Printer Testing
There are thousands of different printers for use with a system
  Simple character
  Graphics
  Monochrome
  Color
No practical test lab could have a version of each unique printer

## Slide 9: Printer Testing
Overview of printers
  Printer Mechanisms
    Typewriter like
      Mechanical impact with ribbon
      One stroke forms one character
    Dot matrix
      Mechanical impact with ribbon
      Wires used to print little dots which form characters
    Ink jet
      Sprays dots of ink on page to form characters and graphics
    Page printers
      Laser, LCD, LED, and thermal transfer

## Slide 10: Printer Testing
Overview of printers
  Various printer control codes and languages
    Control Codes
      Gives specific instruction of how to do special functions
        Print italics or bold
        Change fonts
        Print graphics
    Languages
      PostScript and PCL
      Allows complex control of print functions

## Slide 11: Printer Testing
Overview of printers
  Color Capabilities
    Monochrome, simple color, or true colors
  Interface type
    Serial
      RS-232 (DB25, DB9)
      USB (1.1 and 2.0)
      IEEE 1394 (FireWire)
    Parallel
      IEEE 1284 (Centronics/DB25)
      IEEE-488 (GPIB)

## Slide 12: Printer Testing
Strategies for driving printers
  Unique driver for each printer
    Tons of duplicate code
    Common areas in all must be changed for a spec or function change
  Virtual printer driver
    Common code
    Translation Tables
      Contains the details for specific printers
    Relies that not much fancy stuff will be done by driver

## Slide 13: Printer Testing
Overall strategy for testing printers
  Device independent error
    Error would show regardless of printer attached
  Printer class-specific error
    Error dependant on class of printer attached
    E.g. PostScript, PCL, simple control code
  Driver specific error
    Error for a particular printer group
      E.g. HP LaserJet and compatibles
  Printer specific error
    Error seen with a specific printer
      Zebra bar code printer

## Slide 14: Printer Testing
Testing for functional errors (printing)
  Check to see if the overall printing function works
  Highest level
  Major functions
    Italics, bold, change fonts, etc
    Combine functions
      Bold-italic
    Test functions in different areas
      In headers, footers, paragraphs, citations
  Get any errors at this level fixed before proceeding

## Slide 15: Printer Testing
Testing for class-specific errors
  Choose 3 or 4 printers that are most different from each other
    Should represent different classes
  Thoroughly test these printers
    All features
    All areas of program

## Slide 16: Printer Testing
Testing for driver-specific errors
  For each driver
    Command check
      Does it properly do each function
      E.g. print bold and return to normal ok
    If it does the command in one place most likely it will be correct everywhere else
    Ensure printer defaults and changes from default work
      “Dip-Switches”
      Configuration panels
        Via computer
        Via network

## Slide 17: Printer Testing
Testing for printer-specific errors
  Printers listed on installation menu
    Test all options
      Typically impractical to have all printers available
      Use compatible printers
  Printers that should be on the menu
    Ensure compatible printers are at least documented
  Popular compatibles that aren’t compatible
    Popular printers: test to be sure it really is compatible
  Indistinguishable bad member of a popular class
    Watch out for seemingly identical printers (same name but different operation)

## Slide 18: Printer Testing
Printer test matrix
  Need to keep track of what needs to be tested and what has been tested
  Test matrix
    List of functions and printers
    Spreadsheet helps
    Note options, settings, memory installed, etc. when tested

## Slide 19: Printer Testing
Program area | Print feature | HP5850 (HP5xxx) | HP7410 | Lexmark E102n
Main body | Bold on |  |  | 
 | Bold off |  |  | 
 | Ital. on |  |  | 
 | Ital. off |  |  | 
 | Normal |  |  | 
 | Ital. on Bold on |  |  | 
 | Ital. off |  |  | 
 | Bold off |  |  | 
 | Normal |  |  | 

## Slide 20: Printer Testing
Printer test matrix
  A few feature test notes
    Native fonts
      What are the built in fonts (if any)
      Does program support them
      Can features be mixed properly
    Downloaded fonts
      If printer supports downloaded fonts does it work properly
    Special characters
      If program uses special ASCII or other characters make sure the printer will handle them properly
      Does switching mess up printout

## Slide 21: Printer Testing
Printer test matrix
  A few feature test notes
    Graphics
      Bidirectional printing may cause unacceptable print quality
      Need to disable bidirectional printing for best/acceptable quality
    Graphic resolution
      If printer supports different resolutions need to test all
    Error handling
      Push printer to limit to check error handling
        Max memory
        No paper
        Jams
      Recovery from failure

## Slide 22: Printer Testing
Printer test matrix
  A few feature test notes
    Proportional spacing width tables
      Check width table accurate
        Each font has different table
        May be different even within same printer class
    Graphic formats
      Portrait vs. landscape
      Ensure translation is good for different printers
    Color
      Check mapping from screen colors to print colors is adequate

## Slide 23: Printer Testing
Printer test matrix
  A few feature test notes
    Output formats
      Different page sizes
        U.S.: 8½ x 11, 8½ x 14
        World: A3, A4
      Margins
        Check unprintable areas at page edges
      Check across printer classes
    Expensive forms and paper
      Use plain paper on initial test and compare to real form in initial tests

## Slide 24: Printer Testing
Printer test matrix
  A few feature test notes
    Text and graphic positioning
      Again, check margins
      Are unprintable areas properly avoided
    Streaking, banding, odd unintended fill patterns
      Graphic print algorithms may produce bizzare patterns
        Aliasing, moire patterns

## Slide 25: Printer Testing
Saving, sharing, and reusing printer knowledge
  A lot of time and money has been spent on your test efforts
  Document and share your knowledge for future projects
  Likewise, look for work done by others before you to save time and money
  Try a central database
    Make routines flexible as possible
    Don’t make too flexible so they’re hard to use
  Make access to data easy

## Slide 26: Printer Testing
Tips on automated testing
  Catch 22:
    Early printer testing catches bugs early
      Late changes requires retesting
    Late printer testing swamps developers with bugs late in the project
      May impact schedule

## Slide 27: Printer Testing
Tips on automated testing
  Risks
    Don’t spend too much time automating
      Balance effort spent automating vs. manual effort
    Don’t generate output you won’t or can’t review
      Only generate what you plan or can check, the rest is a waste of time and money
    Watch out for missing printing bugs
      Make bugs easy to find
    Don’t be rigid
      Don’t rerun same tests over and over
      Eventually all bugs will be found by those tests
      Make new tests

## Slide 28: Printer Testing
Tips on automated testing
  Where to save time and improve reliability
    Basic steps
      Planning and developing test
      Acquire printer
      Set up printer
      Run tests
      Return or store printer
    Make the flow easy and efficient as possible

## Slide 29: Printer Testing
Tips on automated testing
  Test files
    Make test results as obvious as possible
      Self explanatory results
        Bold Normal Italics Normal Underline Normal
      Make margins obvious
        123456789a123456789b123…789h12
        223456789a1234 6789b123…789h12
        323456789a123456789b123…789h12
        Note error on second line 15th position
      Use numbers and algorithms to make placement obvious
      Use real data to make sure the output looks good
      For proportional fonts use extreme character sizes
        iiiiiiiiiiiiiiiiiiii
        WWWWWWWWWWWWWWWWWWWW

## Slide 30: Printer Testing
Tips on automated testing
  Reduce setup and teardown time
    Ideal scenario
      Printers in lab with a switchbox
    Realistic
      Print to disc
        Review file contents for errors where possible
        Print rest later when printer available
      Test as many compatible scenarios on one printer
      Evaluate results as soon as possible
        Immediately review printout when printed
        If errors seen double check printer setup
      Test printers on network
        Secure agreements to test on oddball printers someone else has that are impractical for exclusive testing use

## Slide 31: Printer Testing
Tips on automated testing
  Reduce test execution time
    Test on more than one printer at once
      Printing takes time
      Print on as many as you can effectively handle
    Test Automation
      Command set to contain
        Input file name
        Output file or address of printer
        Setup information

## Slide 32: Printer Testing
Tips on automated testing
  Improve test evaluation
    Make everything obvious
    Don’t print (or produce) anything you don’t need
    Print comparison on left, failures on right
    When test files don’t match, print both, label them and highlight differences
    Evaluate output as it comes out of the printer
    Run some tests interactively to test the “interactiveness”
    Make sure the test data is meaningful

## Slide 33: Printer Testing
Tips on automated testing
  Keep the output
    Use interim results for retests
      Was the problem fixed
      Was another problem introduced
    Keep the final printouts of shipped product
      Verify version changes

## Slide 34: Printer Testing
Setting up a printer test lab
  Printers cost money
  Storing printers costs money
  Not have printer on hand costs time  costs money
  Balance the two

## Slide 35: Printer Testing
Setting up a printer test lab
  Get printers on loan
    Impractical to own each printer the product supports
    Borrow printer from the manufacturer
      If your product is popular will be glad to lend
    Borrow from within company
      Someone in the company may be able to lend the print on a short term basis

## Slide 36: Printer Testing
Setting up a printer test lab
  Organize your lab
    Put printers on sturdy shelves
    Space racks
    Keep printers ready to print
    Use switch boxes or networks
    If can’t connect all, keep in safe accessible area
    Use sturdy carts
    Fix what breaks immediately
    Keep reasonable supplies on hand
    Label the printers and keep documentation handy
    Protect the ears

## Slide 37: Device testing
The techniques discussed for printers can apply to other devices

## Slide 38: Device testing
Video Cards
  2 major 3D players
    ATI
      Multiple models/capabilities
        128/256/512 Mb
        Crossfire
    nVidia chip set
      Multiple vendors
      Multiple models
        128/256/512 Mb
        SLI
  Other players
    Intel
      On mother board video
    SiS
  Different buses
    PCI
    AGP
    PCI-Express

## Slide 39: Device testing
Monitors
  CRT
    Various resolution
      800x600, 1024x768, 1280x1024, 1600x1200
  LCD
    Various aspect ratios
      4:3
      16:10
      16:9
    Native resolution
  Plasma
    Ditto

## Slide 40: Device testing
Other devices
  Webcams
  Mice
  Thumb drives
  Sound cards
  Wi-fi cards
  USB devices
  Fire-wire
  Etc.

## Slide 41: Printer Testing
Summary
  Can’t test every possible printer
  Group printers by class
  Test what your users use
  Techniques apply to other devices